## Slide 1
ICSE • CLASS 10 • ELECTRICITY
Resistor Networks, Energy & Power
Series & parallel • Electrical energy & power • The kilowatt-hour • Heating effect

## Slide 2
INTRODUCTION
Learning Objectives
1
Combine resistors in series and in parallel
2
Calculate the equivalent resistance of a network
3
Use electrical energy W = V I t
4
Use electrical power P = V I = I²R = V²/R
5
Convert energy to the commercial unit, the kilowatt-hour
6
Explain the heating effect of an electric current
Notes: Open by previewing these objectives so students know what they should be able to do by the end of the session.

## Slide 3
1
PART 1
Combining Resistors
Series and parallel networks

## Slide 4
COMBINATIONS
Series and Parallel
Series adds; parallel reduces the total
Two ways to connect
• In series, resistors are joined end to end; the same current flows through each.
• Series resistances simply add: R = R₁ + R₂ + R₃.
• In parallel, resistors share the same two ends and the same voltage.
• For parallel: 1/R = 1/R₁ + 1/R₂ + 1/R₃, giving a smaller total than any one.
Notes: Contrast the two: series = same current, voltages add; parallel = same voltage, currents add. Parallel total is always less than the smallest resistor.

## Slide 5
SERIES
Resistors in Series
In a series circuit the same current flows through every resistor and the total resistance is their sum.
R = R₁ + R₂ + R₃ + …
• The current is the same everywhere in the series.
• The supply voltage is shared between the resistors.
• Adding a resistor in series increases the total resistance.
Notes: Series: current common, voltages add up to the supply.

## Slide 6
PARALLEL
Resistors in Parallel
In a parallel circuit every resistor has the same voltage across it, and the currents through them add up.
1/R = 1/R₁ + 1/R₂ + 1/R₃ + …
• The voltage is the same across each branch.
• The total current is the sum of the branch currents.
• The combined resistance is LESS than the smallest resistor.
Notes: Parallel: voltage common, currents add. The equivalent resistance falls — a frequent point of confusion.

## Slide 7
WORKED EXAMPLE
Series and Parallel
Problem. Two 6 Ω resistors are connected (a) in series and (b) in parallel. Find the equivalent resistance in each case.
(a) Series: R = 6 + 6 = 12 Ω
(b) Parallel: 1/R = 1/6 + 1/6 = 2/6 = 1/3
R = 3 Ω
Answer: Series → 12 Ω; Parallel → 3 Ω
Notes: Note the pattern: two equal resistors give 2R in series and R/2 in parallel. A handy shortcut to remember.

## Slide 8
WORKED EXAMPLE
A Mixed Network
Problem. Two 6 Ω resistors are joined in parallel, and this combination is in series with a 4 Ω resistor. Find the total resistance.
Parallel pair: 1/Rp = 1/6 + 1/6 = 2/6 → Rp = 3 Ω
Now in series with 4 Ω: R = Rp + 4
R = 3 + 4 = 7 Ω
Answer: Total resistance = 7 Ω
Notes: Tackle mixed networks in stages: reduce the parallel part first, then add the series resistor.

## Slide 9
BULB BRIGHTNESS
Brighter in Series or in Parallel?
Same bulbs, in series
They share the supply voltage, so each gets less and all glow dimly.
Same bulbs, in parallel
Each gets the full supply voltage, so each glows at full brightness.
If one fails (series)
The single path breaks and all the bulbs go out.
If one fails (parallel)
Only that branch goes out; the others keep glowing — why homes use parallel.
Notes: Classic comparison: parallel bulbs are brighter and independent. Tie to why household wiring is parallel.

## Slide 10
QUIZ 1
Check Your Understanding
5 questions • think before the answer reveals on the next slide

## Slide 11
QUIZ QUESTION
Q1 — Combine Them
Three 3 Ω resistors are connected in series. Their total resistance is:
A
1 Ω
B
3 Ω
C
9 Ω
D
6 Ω

## Slide 12
ANSWER REVEALED
Q1 — Combine Them
Three 3 Ω resistors are connected in series. Their total resistance is:
A
1 Ω
B
3 Ω
✓
9 Ω
D
6 Ω
WHY
In series, resistances add: 3 + 3 + 3 = 9 Ω. Series always gives a total larger than any single resistor.

## Slide 13
QUIZ QUESTION
Q2 — Parallel Pair
Two 4 Ω resistors are connected in parallel. The equivalent resistance is:
A
8 Ω
B
4 Ω
C
2 Ω
D
0.5 Ω

## Slide 14
ANSWER REVEALED
Q2 — Parallel Pair
Two 4 Ω resistors are connected in parallel. The equivalent resistance is:
A
8 Ω
B
4 Ω
✓
2 Ω
D
0.5 Ω
WHY
For two equal resistors in parallel the result is half: 4 / 2 = 2 Ω. The parallel total is always smaller than either resistor.

## Slide 15
QUIZ QUESTION
Q3 — Christmas Lights
In some old light strings, if one bulb fails the whole string goes dark. The bulbs must be connected in:
A
Parallel
B
Series
C
A mixture
D
It cannot be told

## Slide 16
ANSWER REVEALED
Q3 — Christmas Lights
In some old light strings, if one bulb fails the whole string goes dark. The bulbs must be connected in:
A
Parallel
✓
Series
C
A mixture
D
It cannot be told
WHY
In series there is only one path, so a single broken bulb breaks the whole circuit. In parallel, each bulb has its own path and the others stay lit.

## Slide 17
QUIZ QUESTION
Q4 — Brighter Wiring
House lights and sockets are wired in parallel rather than series so that:
A
They share one switch
B
Each appliance gets the full mains voltage and can be switched independently
C
Less copper is needed
D
The current is smaller

## Slide 18
ANSWER REVEALED
Q4 — Brighter Wiring
House lights and sockets are wired in parallel rather than series so that:
A
They share one switch
✓
Each appliance gets the full mains voltage and can be switched independently
C
Less copper is needed
D
The current is smaller
WHY
In parallel every appliance receives the same full mains voltage and can be turned on or off without affecting the others — essential for a household.

## Slide 19
QUIZ QUESTION
Q5 — Reduce the Total
You have three resistors. To get the SMALLEST possible total resistance you should connect them:
A
All in series
B
All in parallel
C
Two in series, one in parallel
D
It makes no difference

## Slide 20
ANSWER REVEALED
Q5 — Reduce the Total
You have three resistors. To get the SMALLEST possible total resistance you should connect them:
A
All in series
✓
All in parallel
C
Two in series, one in parallel
D
It makes no difference
WHY
Parallel connection always gives an equivalent resistance smaller than the smallest resistor, because the current has several paths. Series would give the largest total.

## Slide 21
2
PART 2
Electrical Energy & Power
Paying for electricity and the heating effect

## Slide 22
ENERGY
Electrical Energy
Electrical energy is the work done in driving charge around a circuit.
W = V I t (joules)
• V is the voltage, I the current, t the time in seconds.
• Using V = IR, it can also be written I²Rt or (V²/R) t.
• The SI unit of energy is the joule (J).
Notes: W = VIt, with the I²Rt and V²t/R forms following from Ohm's law. Joule is the SI unit.

## Slide 23
POWER
Electrical Power
Power is the rate at which electrical energy is used or supplied.
P = V I = I² R = V² / R (watt)
• 1 watt = 1 joule per second.
• Choose the form that fits the quantities you are given.
• The power rating of an appliance (e.g. 60 W) tells you its rate of energy use.
Notes: Three forms of power for different given data. Tie to appliance ratings the students see at home.

## Slide 24
WORKED EXAMPLE
Power and Current
Problem. An electric heater is marked 1500 W, 230 V. Find the current it draws and its resistance.
P = V I → I = P / V = 1500 / 230 ≈ 6.5 A
R = V / I = 230 / 6.5 ≈ 35 Ω
(or R = V² / P = 230² / 1500 ≈ 35 Ω)
Answer: I ≈ 6.5 A, R ≈ 35 Ω
Notes: Two routes to R — via I or directly from V²/P. Good chance to show the equivalence.

## Slide 25
KWH
The Kilowatt-Hour
Electricity is sold not in joules but in kilowatt-hours — the energy used by a 1 kW appliance in 1 hour.
Energy (kWh) = power (kW) × time (hours)
• 1 kWh = 1000 W × 3600 s = 3.6 × 10⁶ J.
• It is the 'unit' on your electricity bill.
• Cost = number of units × price per unit.
Notes: The kWh is the commercial 'unit'. Convert to joules once so students see the size of it.

## Slide 26
WORKED EXAMPLE
Cost of Electricity
Problem. A 2 kW heater runs for 3 hours each day. At ₹6 per unit (kWh), find the cost for 30 days.
Energy per day = 2 kW × 3 h = 6 kWh
Energy in 30 days = 6 × 30 = 180 kWh (units)
Cost = 180 × ₹6 = ₹1080
Answer: Cost for the month = ₹1080
Notes: Units (kWh) = kW × hours, then multiply by price. A real-life calculation students can do at home.

## Slide 27
HEATING EFFECT
The Heating Effect of Current
H = I² R t
• Why it heats Moving electrons collide with atoms, giving up energy as heat: H = I²Rt.
• Depends on I² Doubling the current quadruples the heat produced.
• Useful Heaters, electric irons, geysers, toasters and filament lamps.
• Unwanted Overheated wires waste energy and can cause fires — hence fuses.
Notes: Heating H = I²Rt; the I² dependence is key. Useful in heaters, a hazard in overloaded wiring.

## Slide 28
WRAP UP
Quick Recap
✓ Series — R = R₁ + R₂ + …; same current
✓ Parallel — 1/R = 1/R₁ + 1/R₂ + …; same voltage, smaller total
✓ Energy — W = V I t (joules)
✓ Power — P = V I = I²R = V²/R (watts)
✓ kWh — units = kW × hours; cost = units × price
✓ Heating effect — H = I²R t; useful in heaters, controlled by fuses
Notes: Rapid recap; the kWh cost calculation and I²Rt heating are exam staples.

## Slide 29
QUIZ 2
Final Check — Energy & Power
5 questions • think before the answer reveals on the next slide

## Slide 30
QUIZ QUESTION
Q1 — Energy Used
A 100 W bulb is left on for 10 hours. The energy it uses, in units (kWh), is:
A
1 unit
B
10 units
C
100 units
D
1000 units

## Slide 31
ANSWER REVEALED
Q1 — Energy Used
A 100 W bulb is left on for 10 hours. The energy it uses, in units (kWh), is:
✓
1 unit
B
10 units
C
100 units
D
1000 units
WHY
Energy = power × time = 0.1 kW × 10 h = 1 kWh = 1 unit. Convert the 100 W to 0.1 kW first.

## Slide 32
QUIZ QUESTION
Q2 — Double the Current
If the current through a heating element is doubled, the heat produced per second becomes:
A
Doubled
B
Halved
C
Four times as great
D
Unchanged

## Slide 33
ANSWER REVEALED
Q2 — Double the Current
If the current through a heating element is doubled, the heat produced per second becomes:
A
Doubled
B
Halved
✓
Four times as great
D
Unchanged
WHY
Heat per second = I²R. Because it depends on the square of the current, doubling I multiplies the heat by 2² = 4.

## Slide 34
QUIZ QUESTION
Q3 — Which Heats More?
Two appliances run on the same mains voltage. The one with the higher power rating draws:
A
Less current and has more resistance
B
More current and has less resistance
C
The same current
D
No current

## Slide 35
ANSWER REVEALED
Q3 — Which Heats More?
Two appliances run on the same mains voltage. The one with the higher power rating draws:
A
Less current and has more resistance
✓
More current and has less resistance
C
The same current
D
No current
WHY
At fixed voltage, P = V²/R, so higher power means lower resistance; and P = VI means it also draws more current. A 2 kW heater pulls more current than a 60 W bulb.

## Slide 36
QUIZ QUESTION
Q4 — Cost
An air-conditioner of 1.5 kW runs 8 hours a day. At ₹5 per unit, the daily cost is:
A
₹12
B
₹60
C
₹40
D
₹75

## Slide 37
ANSWER REVEALED
Q4 — Cost
An air-conditioner of 1.5 kW runs 8 hours a day. At ₹5 per unit, the daily cost is:
A
₹12
✓
₹60
C
₹40
D
₹75
WHY
Energy = 1.5 kW × 8 h = 12 units. Cost = 12 × ₹5 = ₹60 per day.

## Slide 38
QUIZ QUESTION
Q5 — Same Bulb, Half Voltage
A bulb of fixed resistance is run at half its normal voltage. The power it now uses is:
A
Half
B
One quarter
C
The same
D
Double

## Slide 39
ANSWER REVEALED
Q5 — Same Bulb, Half Voltage
A bulb of fixed resistance is run at half its normal voltage. The power it now uses is:
A
Half
✓
One quarter
C
The same
D
Double
WHY
P = V²/R with R fixed, so power depends on the square of the voltage. Half the voltage gives (½)² = ¼ of the power — which is why a dimmed bulb is much dimmer.

## Slide 40
Powering Everyday Life
Series or parallel, joules or units — the same simple formulae run every circuit in your home.