## Slide 1
SIMPLE MACHINES
Simple Machines — Workout
Practice covering Simple Machines Lessons 1 & 2

## Slide 2
WORKOUT SCOPE
What This Workout Covers
Syllabus for this practice session
• Simple Machines 1 Work & energy, machines, principle of a machine, efficiency, ideal & actual machine, functions, mechanical advantage, levers, principle of a lever, orders of levers.
• Simple Machines 2 Pulley & its MA, wheel and axle, inclined plane, wedge, screw, care of machines.
Notes: State the scope up front: every question is drawn only from these lessons. Nothing outside this syllabus appears.

## Slide 3
1
SECTION A
Multiple-Choice Questions
20 questions — choose the single best option

## Slide 4
SECTION A
Multiple-Choice Practice
20 questions • think before the answer reveals on the next slide

## Slide 5
QUIZ QUESTION
Q1 - Work
A porter carries a heavy suitcase on his head and walks 50 m along a level platform at steady speed. The work he does against gravity is:
A
Equal to the suitcase's weight
B
Large and positive
C
Negative
D
Zero

## Slide 6
QUIZ QUESTION
Q1 - Work
A porter carries a heavy suitcase on his head and walks 50 m along a level platform at steady speed. The work he does against gravity is:
A
Equal to the suitcase's weight
B
Large and positive
C
Negative
D
Zero
✓
Why His supporting force is vertical (up) but the motion is horizontal, so the displacement in the direction of that force is zero — hence the work done against gravity is zero.

## Slide 7
QUIZ QUESTION
Q2 - Units
Which of the following is NOT a unit of work or energy?
A
Erg
B
Joule
C
Newton metre
D
Watt

## Slide 8
QUIZ QUESTION
Q2 - Units
Which of the following is NOT a unit of work or energy?
A
Erg
B
Joule
C
Newton metre
D
Watt
✓
Why The watt is the unit of power (1 W = 1 J/s), not of work or energy. Joule, newton-metre and erg are all units of energy.

## Slide 9
QUIZ QUESTION
Q3 - Machine functions
Which of these is NOT something a simple machine can do for us?
A
Change the direction of the applied force
B
Let us apply the effort at a convenient point
C
Multiply a small effort to move a large load
D
Create extra energy to do more work

## Slide 10
QUIZ QUESTION
Q3 - Machine functions
Which of these is NOT something a simple machine can do for us?
A
Change the direction of the applied force
B
Let us apply the effort at a convenient point
C
Multiply a small effort to move a large load
D
Create extra energy to do more work
✓
Why A machine never creates energy — it only transfers and redistributes the work put into it. Output work can never exceed input work.

## Slide 11
QUIZ QUESTION
Q4 - Mechanical advantage
A machine overcomes a load of 600 N using an effort of 150 N. Its mechanical advantage is:
A
4
B
450 N
C
750 N
D
0.25

## Slide 12
QUIZ QUESTION
Q4 - Mechanical advantage
A machine overcomes a load of 600 N using an effort of 150 N. Its mechanical advantage is:
A
4
✓
B
450 N
C
750 N
D
0.25
Why MA = Load / Effort = 600 / 150 = 4. It is a ratio of two forces, so it has no unit.

## Slide 13
QUIZ QUESTION
Q5 - Efficiency
A machine is supplied 500 J of work and does 400 J of useful work. Its efficiency is:
A
125%
B
20%
C
80%
D
100 J

## Slide 14
QUIZ QUESTION
Q5 - Efficiency
A machine is supplied 500 J of work and does 400 J of useful work. Its efficiency is:
A
125%
B
20%
C
80%
✓
D
100 J
Why Efficiency = (useful work output / work input) x 100 = (400 / 500) x 100 = 80%.

## Slide 15
QUIZ QUESTION
Q6 - Efficiency
The efficiency of every real machine is less than 100% mainly because:
A
the effort is applied in the wrong direction
B
mechanical advantage is always less than one
C
the load is always too heavy
D
some input work is wasted against friction and in moving the machine's own parts

## Slide 16
QUIZ QUESTION
Q6 - Efficiency
The efficiency of every real machine is less than 100% mainly because:
A
the effort is applied in the wrong direction
B
mechanical advantage is always less than one
C
the load is always too heavy
D
some input work is wasted against friction and in moving the machine's own parts
✓
Why Part of the input work is always used up against friction and in lifting the machine's own moving parts, so useful output is always less than the input.

## Slide 17
QUIZ QUESTION
Q7 - Ideal machine
For an ideal (frictionless) machine, which relation is true?
A
MA > VR
B
MA = VR
C
MA = 0
D
MA < VR

## Slide 18
QUIZ QUESTION
Q7 - Ideal machine
For an ideal (frictionless) machine, which relation is true?
A
MA > VR
B
MA = VR
✓
C
MA = 0
D
MA < VR
Why An ideal machine has no friction and weightless parts, so its efficiency is 100% and its mechanical advantage equals its velocity ratio (MA = VR).

## Slide 19
QUIZ QUESTION
Q8 - Lever
The fixed point about which a lever turns is called the:
A
pivot arm
B
fulcrum
C
effort arm
D
load

## Slide 20
QUIZ QUESTION
Q8 - Lever
The fixed point about which a lever turns is called the:
A
pivot arm
B
fulcrum
✓
C
effort arm
D
load
Why A lever turns about a fixed point called the fulcrum. The other two points are where the load and the effort act.

## Slide 21
QUIZ QUESTION
Q9 - Lever principle
A crowbar lifts an 800 N rock. The load is 20 cm from the fulcrum and the effort is applied 80 cm from it. The ideal effort needed is:
A
800 N
B
3200 N
C
200 N
D
160 N

## Slide 22
QUIZ QUESTION
Q9 - Lever principle
A crowbar lifts an 800 N rock. The load is 20 cm from the fulcrum and the effort is applied 80 cm from it. The ideal effort needed is:
A
800 N
B
3200 N
C
200 N
✓
D
160 N
Why By the principle of the lever, Load x load-arm = Effort x effort-arm: 800 x 20 = E x 80, so E = 200 N.

## Slide 23
QUIZ QUESTION
Q10 - Levers
Which of the following is a first-order lever?
A
A pair of sugar tongs
B
A pair of scissors
C
A nutcracker
D
A wheelbarrow

## Slide 24
QUIZ QUESTION
Q10 - Levers
Which of the following is a first-order lever?
A
A pair of sugar tongs
B
A pair of scissors
✓
C
A nutcracker
D
A wheelbarrow
Why In a pair of scissors the fulcrum (the rivet) lies between the effort and the load, so it is a first-order lever. The others are second- or third-order levers.

## Slide 25
QUIZ QUESTION
Q11 - Levers
The mechanical advantage of a second-order lever is always:
A
less than 1
B
greater than 1
C
equal to 1
D
zero

## Slide 26
QUIZ QUESTION
Q11 - Levers
The mechanical advantage of a second-order lever is always:
A
less than 1
B
greater than 1
✓
C
equal to 1
D
zero
Why In a second-order lever the load lies between the fulcrum and the effort, so the effort-arm is always longer than the load-arm, giving MA > 1 (a force multiplier).

## Slide 27
QUIZ QUESTION
Q12 - Levers
A pair of forceps (tongs) has a mechanical advantage less than one. We still use such third-order levers because they:
A
give a gain in speed and a wider range of movement
B
reduce friction
C
change the direction of the force
D
multiply the effort

## Slide 28
QUIZ QUESTION
Q12 - Levers
A pair of forceps (tongs) has a mechanical advantage less than one. We still use such third-order levers because they:
A
give a gain in speed and a wider range of movement
✓
B
reduce friction
C
change the direction of the force
D
multiply the effort
Why A third-order lever has its effort between the fulcrum and load, so MA < 1; it is used because the load end moves faster and over a larger distance than the effort.

## Slide 29
QUIZ QUESTION
Q13 - Levers
The human forearm lifting a load held in the hand acts as a lever of which order?
A
Second order
B
No order
C
Third order
D
First order

## Slide 30
QUIZ QUESTION
Q13 - Levers
The human forearm lifting a load held in the hand acts as a lever of which order?
A
Second order
B
No order
C
Third order
✓
D
First order
Why The elbow is the fulcrum and the biceps (effort) acts between the elbow and the load in the hand, so the forearm is a third-order lever.

## Slide 31
QUIZ QUESTION
Q14 - Pulley
A single fixed pulley is used to draw water from a well mainly because it:
A
lets you pull down to raise the bucket up (changes the direction of effort)
B
has a mechanical advantage of 2
C
reduces the weight of the water
D
multiplies the effort

## Slide 32
QUIZ QUESTION
Q14 - Pulley
A single fixed pulley is used to draw water from a well mainly because it:
A
lets you pull down to raise the bucket up (changes the direction of effort)
✓
B
has a mechanical advantage of 2
C
reduces the weight of the water
D
multiplies the effort
Why A single fixed pulley has an ideal MA of 1; it does not reduce the effort but lets you apply it in a convenient (downward) direction.

## Slide 33
QUIZ QUESTION
Q15 - Pulley
The ideal mechanical advantage of a single movable pulley is:
A
1
B
4
C
0.5
D
2

## Slide 34
QUIZ QUESTION
Q15 - Pulley
The ideal mechanical advantage of a single movable pulley is:
A
1
B
4
C
0.5
D
2
✓
Why In a single movable pulley the load is shared by two segments of the rope, so the effort is half the load and the ideal MA is 2.

## Slide 35
QUIZ QUESTION
Q16 - Wheel and axle
A steering wheel of radius 20 cm turns an axle of radius 4 cm. Its ideal mechanical advantage is:
A
5
B
0.2
C
16
D
80

## Slide 36
QUIZ QUESTION
Q16 - Wheel and axle
A steering wheel of radius 20 cm turns an axle of radius 4 cm. Its ideal mechanical advantage is:
A
5
✓
B
0.2
C
16
D
80
Why For a wheel and axle, MA = radius of wheel / radius of axle = 20 / 4 = 5.

## Slide 37
QUIZ QUESTION
Q17 - Inclined plane
A 12 m long ramp rises to a height of 3 m. The ideal mechanical advantage of the ramp is:
A
36
B
4
C
9
D
0.25

## Slide 38
QUIZ QUESTION
Q17 - Inclined plane
A 12 m long ramp rises to a height of 3 m. The ideal mechanical advantage of the ramp is:
A
36
B
4
✓
C
9
D
0.25
Why For an inclined plane, MA = length of slope / height = 12 / 3 = 4.

## Slide 39
QUIZ QUESTION
Q18 - Wedge
A wedge, such as the blade of an axe, is essentially:
A
a single lever
B
a wheel and axle
C
two inclined planes joined back to back
D
a movable pulley

## Slide 40
QUIZ QUESTION
Q18 - Wedge
A wedge, such as the blade of an axe, is essentially:
A
a single lever
B
a wheel and axle
C
two inclined planes joined back to back
✓
D
a movable pulley
Why A wedge is made of two inclined planes joined along their slopes; it is used to separate, split or cut, as an axe splits wood.

## Slide 41
QUIZ QUESTION
Q19 - Screw
A screw can be regarded as:
A
a first-order lever
B
two pulleys in series
C
an inclined plane wrapped around a cylinder
D
a flat wedge

## Slide 42
QUIZ QUESTION
Q19 - Screw
A screw can be regarded as:
A
a first-order lever
B
two pulleys in series
C
an inclined plane wrapped around a cylinder
✓
D
a flat wedge
Why The thread of a screw is simply an inclined plane wound around a cylinder; the distance between two threads is its pitch.

## Slide 43
QUIZ QUESTION
Q20 - Care of machines
Oiling and greasing the moving parts of a machine raises its efficiency because it:
A
reduces the friction between the parts
B
increases its mechanical advantage
C
increases the load it can lift
D
creates extra energy

## Slide 44
QUIZ QUESTION
Q20 - Care of machines
Oiling and greasing the moving parts of a machine raises its efficiency because it:
A
reduces the friction between the parts
✓
B
increases its mechanical advantage
C
increases the load it can lift
D
creates extra energy
Why Oil reduces friction between moving parts, so less input work is wasted as heat and the efficiency rises (closer to the ideal).

## Slide 45
2
SECTION B
Subjective Questions
5 long-answer questions — write full answers

## Slide 46
SECTION B
Subjective Practice
5 questions • think before the answer reveals on the next slide

## Slide 47
SUBJECTIVE QUESTION
Q1 — Work
Define work and state its SI unit. A boy pushes hard against a wall with a force of 200 N but the wall does not move. How much work does he do? Give a reason.
[ 3 marks ]
Attempt this in your notebook before the answer reveals.
Notes: Subjective practice on 'Work'. Give students time to write a full answer, then reveal the model points.

## Slide 48
MODEL ANSWER
Q1 — Work
Q. Define work and state its SI unit. A boy pushes hard against a wall with a force of 200 N but the wall does not move. How much work does he do? Give a reason.
• Work is done when a force acts on a body and the body moves in the direction of the force: Work = Force x distance moved (W = F x s).
• SI unit of work is the joule (J); 1 J = 1 N moved through 1 m.
• Work done = 0, because the wall does not move (displacement = 0), so no work is done however large the force applied.
Notes: Model answer for Q1. Award up to 3 marks; accept equivalent correct wording.

## Slide 49
SUBJECTIVE QUESTION
Q2 — MA, VR & Efficiency
Define mechanical advantage and velocity ratio. Why is the efficiency of an actual machine always less than 100%? Write the relation between efficiency, MA and VR.
[ 4 marks ]
Attempt this in your notebook before the answer reveals.
Notes: Subjective practice on 'MA, VR & Efficiency'. Give students time to write a full answer, then reveal the model points.

## Slide 50
MODEL ANSWER
Q2 — MA, VR & Efficiency
Q. Define mechanical advantage and velocity ratio. Why is the efficiency of an actual machine always less than 100%? Write the relation between efficiency, MA and VR.
• Mechanical advantage (MA) = Load / Effort; it tells how many times a machine multiplies the effort (no unit).
• Velocity ratio (VR) = distance moved by effort / distance moved by load (no unit).
• Efficiency is always < 100% because some input work is always used up against friction and in moving the machine's own parts, so useful output < input.
• Relation: Efficiency = MA / VR.
Notes: Model answer for Q2. Award up to 4 marks; accept equivalent correct wording.

## Slide 51
SUBJECTIVE QUESTION
Q3 — Principle of a lever
State the principle of a lever. A see-saw has a 400 N child sitting 1.5 m from the pivot. Where must a 600 N child sit on the other side to balance it?
[ 3 marks ]
Attempt this in your notebook before the answer reveals.
Notes: Subjective practice on 'Principle of a lever'. Give students time to write a full answer, then reveal the model points.

## Slide 52
MODEL ANSWER
Q3 — Principle of a lever
Q. State the principle of a lever. A see-saw has a 400 N child sitting 1.5 m from the pivot. Where must a 600 N child sit on the other side to balance it?
• Principle (law of moments): when a lever is balanced, Load x load-arm = Effort x effort-arm (anticlockwise moment = clockwise moment).
• 400 x 1.5 = 600 x d, so 600 = 600 d.
• d = 1.0 m from the pivot on the opposite side.
Notes: Model answer for Q3. Award up to 3 marks; accept equivalent correct wording.

## Slide 53
SUBJECTIVE QUESTION
Q4 — Orders of levers
Name the three orders of levers. For each, state the relative position of the load, effort and fulcrum, and give one example.
[ 4 marks ]
Attempt this in your notebook before the answer reveals.
Notes: Subjective practice on 'Orders of levers'. Give students time to write a full answer, then reveal the model points.

## Slide 54
MODEL ANSWER
Q4 — Orders of levers
Q. Name the three orders of levers. For each, state the relative position of the load, effort and fulcrum, and give one example.
• First order: fulcrum lies between the load and the effort — e.g. a see-saw, a pair of scissors or a crowbar.
• Second order: load lies between the fulcrum and the effort — e.g. a wheelbarrow or a nutcracker (MA always > 1).
• Third order: effort lies between the fulcrum and the load — e.g. forceps, a fishing rod or the human forearm (MA always < 1).
Notes: Model answer for Q4. Award up to 4 marks; accept equivalent correct wording.

## Slide 55
SUBJECTIVE QUESTION
Q5 — Inclined plane
What is an inclined plane? A man rolls a 500 N barrel up a 4 m long plank onto a platform 1 m high. Find the ideal mechanical advantage and the ideal effort needed.
[ 3 marks ]
Attempt this in your notebook before the answer reveals.
Notes: Subjective practice on 'Inclined plane'. Give students time to write a full answer, then reveal the model points.

## Slide 56
MODEL ANSWER
Q5 — Inclined plane
Q. What is an inclined plane? A man rolls a 500 N barrel up a 4 m long plank onto a platform 1 m high. Find the ideal mechanical advantage and the ideal effort needed.
• An inclined plane is a sloping flat surface used to raise a load with less effort applied over a longer distance.
• Ideal MA = length of slope / height = 4 / 1 = 4.
• Ideal effort = Load / MA = 500 / 4 = 125 N.
Notes: Model answer for Q5. Award up to 3 marks; accept equivalent correct wording.

## Slide 57
Well Practised!
Re-check every numerical you missed and revise the orders of levers and the MA of each machine before the test.