## Slide 1
ICSE • CLASS 10 • ELECTRICITY
Earthing, Plugs & Safety
Earthing • The three-pin plug • Colour coding • Electrical safety

## Slide 2
INTRODUCTION
Learning Objectives
1
Explain the purpose of earthing an appliance
2
Identify the three pins of a plug and their wires
3
State the colour code of live, neutral and earth wires
4
Explain why the earth pin is longer and thicker
5
Describe the danger of high-tension wires
6
List safety precautions for using electricity
Notes: Open by previewing these objectives so students know what they should be able to do by the end of the session.

## Slide 3
1
PART 1
Earthing & the Three-Pin Plug
How an appliance is made safe to touch

## Slide 4
EARTHING
Why We Earth Appliances
Earthing connects the metal body of an appliance to the ground through the earth wire, so it can never reach a dangerous voltage.
• If the live wire touches the metal body, current flows safely to earth instead of through a person.
• This large current also blows the fuse, cutting off the supply.
• Without earthing, the body would stay live and give a shock when touched.
Notes: Earthing gives a safe, low-resistance path for fault current — protecting the user and blowing the fuse.

## Slide 5
THREE-PIN PLUG
Inside a Three-Pin Plug
Earth pin: longer and thicker; fuse in the live
Live, neutral & earth
• The three pins are live (L), neutral (N) and earth (E).
• The earth pin is longer, so it connects first and disconnects last.
• It is also thicker to carry a large fault current safely.
• The fuse is fitted in the live wire of the plug.
Notes: Walk through the three pins. The longer earth pin connects first (safety); the fuse is in the live wire.

## Slide 6
COLOUR CODE
Colour Coding of Wires
Live — brown
Carries the dangerous 230 V supply (older code: red).
Neutral — blue
Completes the circuit, near 0 V (older code: black).
Earth — green/yellow
The safety wire to the ground (older code: green).
Why colours
So wires are connected to the correct terminals every time.
Notes: Memorise the modern code: brown live, blue neutral, green/yellow earth. Wrong connections are dangerous.

## Slide 7
EARTH PIN
Why the Earth Pin Is Special
First to connect, last to leave
• Longer It makes contact first when plugging in, so the appliance is earthed before it is live.
• Thicker It can safely carry a large fault current to the ground.
• Opens the shutters In many sockets the long earth pin pushes open safety shutters over the live and neutral holes.
• Connected to the body Inside the appliance the earth wire is joined to its metal casing.
Notes: The earth pin's length and thickness are favourite exam points: connects first, carries fault current, opens shutters.

## Slide 8
QUIZ 1
Check Your Understanding
4 questions • think before the answer reveals on the next slide

## Slide 9
QUIZ QUESTION
Q1 — Fault to the Body
The live wire inside a metal toaster comes loose and touches the casing. If the toaster is properly earthed, what happens?
A
The casing becomes live and dangerous
B
A large current flows to earth and blows the fuse, cutting the supply
C
Nothing changes
D
The toaster runs faster

## Slide 10
ANSWER REVEALED
Q1 — Fault to the Body
The live wire inside a metal toaster comes loose and touches the casing. If the toaster is properly earthed, what happens?
A
The casing becomes live and dangerous
✓
A large current flows to earth and blows the fuse, cutting the supply
C
Nothing changes
D
The toaster runs faster
WHY
Earthing offers a low-resistance path to ground. The fault current is large, so the fuse melts and disconnects the supply, leaving the casing safe to touch.

## Slide 11
QUIZ QUESTION
Q2 — Colour Check
In the modern colour code, the wire that is brown is the:
A
Earth wire
B
Neutral wire
C
Live wire
D
Signal wire

## Slide 12
ANSWER REVEALED
Q2 — Colour Check
In the modern colour code, the wire that is brown is the:
A
Earth wire
B
Neutral wire
✓
Live wire
D
Signal wire
WHY
The modern code is brown = live, blue = neutral, green/yellow = earth. The brown live wire carries the dangerous 230 V.

## Slide 13
QUIZ QUESTION
Q3 — Longer Pin
The earth pin of a plug is made longer than the other two so that:
A
It looks different
B
The appliance is earthed first, before the live pin makes contact
C
It carries the current
D
It fits more tightly

## Slide 14
ANSWER REVEALED
Q3 — Longer Pin
The earth pin of a plug is made longer than the other two so that:
A
It looks different
✓
The appliance is earthed first, before the live pin makes contact
C
It carries the current
D
It fits more tightly
WHY
The longer earth pin enters the socket first and leaves last, so the appliance is safely earthed throughout the moment it is live — and it often opens the socket's safety shutters too.

## Slide 15
QUIZ QUESTION
Q4 — No Earth
A plastic-bodied hair dryer with no metal parts is often sold with only two pins (no earth) because:
A
Plastic conducts electricity
B
Its non-conducting case can never become live, so earthing is not needed
C
It uses no current
D
Earthing would damage it

## Slide 16
ANSWER REVEALED
Q4 — No Earth
A plastic-bodied hair dryer with no metal parts is often sold with only two pins (no earth) because:
A
Plastic conducts electricity
✓
Its non-conducting case can never become live, so earthing is not needed
C
It uses no current
D
Earthing would damage it
WHY
Earthing protects a conducting (metal) body. A fully insulated plastic body cannot give a shock even if a wire touches it, so such 'double-insulated' devices need no earth pin.

## Slide 17
2
PART 2
High-Tension Wires & Safety
Respecting the dangers of electricity

## Slide 18
HIGH TENSION
High-Tension (HT) Wires
Why HT lines are kept out of reach
• Very high voltage Transmission lines carry tens of thousands of volts.
• Bare and high up They are uninsulated, so they are strung high on tall pylons, out of reach.
• Keep away Never fly kites or raise poles near them — electricity can jump (arc) across a gap.
• Warning signs Danger boards and wide clearances keep people and vehicles at a safe distance.
Notes: HT wires are bare and lethal; height and distance are the safety measures. Stress kite/pole dangers.

## Slide 19
SAFETY
Safety Precautions With Electricity
Dry hands
Never touch switches or appliances with wet hands — water conducts electricity.
Right fuse
Always use a fuse of the correct rating; never replace it with thick wire.
Earth metal appliances
Connect the earth pin; do not bypass it.
Repairs off
Switch off and unplug before repairing or cleaning an appliance.
Notes: Practical safety rules. Connect each to the physics: water conducts, correct fuse protects, earthing saves lives.

## Slide 20
MORE SAFETY
Good Habits That Save Lives
Everyday electrical sense
• No overloading Avoid plugging many high-power appliances into one socket.
• Good insulation Replace frayed or damaged wires and cracked plugs promptly.
• Three-pin for metal Always use an earthed three-pin plug for metal-bodied appliances.
• Keep water away Keep electrical points away from taps, sinks and bathrooms unless specially protected.
Notes: Reinforce habits: no overloading, good insulation, earthing, water awareness.

## Slide 21
DOUBLE INSULATION
Double-Insulated Appliances
Two layers
The live parts are insulated, and the whole casing is a second layer of insulation.
No earth needed
Because the case can never become live, no earth wire is required.
The symbol
Marked with a 'square within a square' symbol.
Examples
Plastic hair dryers, electric shavers and many power tools.
Notes: Double insulation is an alternative to earthing for plastic-bodied devices — two independent layers of insulation.

## Slide 22
ELECTRIC SHOCK
If Someone Gets an Electric Shock
Cut the supply first
• Switch off the mains supply immediately — do not touch the person while they are still connected.
• If you cannot reach the switch, push them away using a dry, non-conducting object like wood.
• Never use your bare hands or anything wet or metal.
• Once they are clear, call for medical help and give first aid if trained.
Notes: Emphasise: isolate the supply before touching the casualty, and only use dry, insulating materials.

## Slide 23
WRAP UP
Quick Recap
✓ Earthing — safe path to ground; protects user and blows the fuse
✓ Three pins — live, neutral, earth; fuse in the live wire
✓ Colour code — brown live, blue neutral, green/yellow earth
✓ Earth pin — longer and thicker — connects first, carries fault current
✓ HT wires — very high voltage, bare, kept high and out of reach
✓ Safety — dry hands, correct fuse, earthing, switch off to repair
Notes: Rapid recap; the earthing mechanism and colour code are the most examined points.

## Slide 24
QUIZ 2
Final Check — Safety
5 questions • think before the answer reveals on the next slide

## Slide 25
QUIZ QUESTION
Q1 — Wet Hands
Touching an electric switch with wet hands is dangerous because:
A
Water repels electricity
B
Water conducts electricity, lowering your resistance and allowing a larger shock current
C
Switches dislike water
D
It increases the voltage

## Slide 26
ANSWER REVEALED
Q1 — Wet Hands
Touching an electric switch with wet hands is dangerous because:
A
Water repels electricity
✓
Water conducts electricity, lowering your resistance and allowing a larger shock current
C
Switches dislike water
D
It increases the voltage
WHY
Wet skin has a much lower resistance than dry skin, so for the same voltage a far larger and more dangerous current can flow through the body.

## Slide 27
QUIZ QUESTION
Q2 — Thick Wire as Fuse
Replacing a blown fuse with a thick copper wire is dangerous because the thick wire:
A
Melts too easily
B
Will not melt on an overload, so the wiring can overheat and catch fire
C
Carries no current
D
Increases the voltage

## Slide 28
ANSWER REVEALED
Q2 — Thick Wire as Fuse
Replacing a blown fuse with a thick copper wire is dangerous because the thick wire:
A
Melts too easily
✓
Will not melt on an overload, so the wiring can overheat and catch fire
C
Carries no current
D
Increases the voltage
WHY
A fuse is meant to be the weak link that melts first. A thick copper wire can carry a huge current without melting, so it removes the protection and the wiring itself may overheat.

## Slide 29
QUIZ QUESTION
Q3 — Kite Warning
Why must you never fly a kite near high-tension power lines?
A
The kite may get dirty
B
Electricity can arc across to a wet string or the kite, giving a fatal shock
C
The lines will fall
D
The kite flies too high

## Slide 30
ANSWER REVEALED
Q3 — Kite Warning
Why must you never fly a kite near high-tension power lines?
A
The kite may get dirty
✓
Electricity can arc across to a wet string or the kite, giving a fatal shock
C
The lines will fall
D
The kite flies too high
WHY
At tens of thousands of volts, current can jump across a small air gap to a kite or a damp string, sending a lethal current down to the person holding it.

## Slide 31
QUIZ QUESTION
Q4 — Bird on a Wire
A bird can sit safely on a single bare power line because:
A
Its feet are insulated
B
There is no potential difference across its body — both feet are on the same wire
C
Birds do not conduct
D
The wire is switched off

## Slide 32
ANSWER REVEALED
Q4 — Bird on a Wire
A bird can sit safely on a single bare power line because:
A
Its feet are insulated
✓
There is no potential difference across its body — both feet are on the same wire
C
Birds do not conduct
D
The wire is switched off
WHY
Both feet touch the same point, so there is almost no voltage difference across the bird and almost no current through it. Touching a second wire or the ground would be fatal.

## Slide 33
QUIZ QUESTION
Q5 — Before Repair
Before repairing an electrical appliance you should always first:
A
Wet your hands
B
Switch off and unplug it from the mains
C
Increase the current
D
Remove the earth wire

## Slide 34
ANSWER REVEALED
Q5 — Before Repair
Before repairing an electrical appliance you should always first:
A
Wet your hands
✓
Switch off and unplug it from the mains
C
Increase the current
D
Remove the earth wire
WHY
Disconnecting the appliance from the live supply removes the source of danger, so no current can flow through you while you work on it.

## Slide 35
Stay Safe With Electricity
Earthing, the right fuse and a little caution turn a deadly force into a everyday convenience.