## Slide 1
ICSE • CLASS 10 • ELECTRICITY
Resistance & Cells
Factors affecting resistance • Resistivity • EMF & internal resistance

## Slide 2
INTRODUCTION
Learning Objectives
1
Distinguish ohmic and non-ohmic conductors
2
List the factors that affect the resistance of a wire
3
Define specific resistance (resistivity) and use R = ρL/A
4
Choose suitable materials for wires and heating elements
5
Describe superconductors
6
Define EMF, terminal voltage and internal resistance of a cell
Notes: Open by previewing these objectives so students know what they should be able to do by the end of the session.

## Slide 3
1
PART 1
What Resistance Depends On
Why some wires resist more than others

## Slide 4
OHMIC OR NOT
Ohmic and Non-Ohmic Conductors
Ohmic
Obey Ohm's law: V–I graph is a straight line, e.g. metal wires at constant temperature.
Non-ohmic
Do not obey Ohm's law: V–I graph is curved, e.g. a filament bulb, a diode.
Why bulbs curve
The filament heats up, its resistance rises, so the graph bends.
Still useful
Non-ohmic devices like diodes are vital in electronics.
Notes: Ohmic = straight line; non-ohmic = curved. The heating filament is the standard non-ohmic example.

## Slide 5
FACTORS
What Affects a Wire's Resistance
Length
Resistance is proportional to length — a longer wire has more resistance.
Area
Resistance is inversely proportional to cross-sectional area — a thicker wire resists less.
Material
Different materials have different resistivities.
Temperature
For metals, resistance increases as temperature rises.
Notes: Four factors. Length ↑ → R ↑; area ↑ → R ↓; plus material and temperature. These feed straight into the resistivity formula.

## Slide 6
RESISTIVITY
Specific Resistance (Resistivity)
The resistance of a wire depends on its length and area through the resistivity ρ of its material.
R = ρ L / A (ρ in ohm-metre, Ω m)
• L is the length, A the cross-sectional area.
• Resistivity ρ is a property of the material, not the shape.
• Good conductors (copper, silver) have very low resistivity.
Notes: R = ρL/A links the factors quantitatively. Stress ρ depends only on material (and temperature), not size.

## Slide 7
WORKED EXAMPLE
Using R = ρL/A
Problem. A wire is 2 m long with cross-sectional area 0.5 mm² (0.5 × 10⁻⁶ m²) and resistivity 1.0 × 10⁻⁶ Ω m. Find its resistance.
R = ρ L / A
R = (1.0 × 10⁻⁶ × 2) / (0.5 × 10⁻⁶)
R = (2.0 × 10⁻⁶) / (0.5 × 10⁻⁶) = 4 Ω
Answer: Resistance R = 4 Ω
Notes: Keep the powers of ten lined up. The micro-factors cancel, leaving a clean number.

## Slide 8
CHOOSING MATERIALS
The Right Wire for the Job
Copper for wiring
Very low resistivity, so it carries current with little loss.
Nichrome for heaters
High resistivity and a high melting point — it gets hot without melting.
Tungsten for filaments
Very high melting point, so it glows white-hot in a bulb without breaking.
Fuse wire
Low melting point, so it melts and breaks the circuit if the current is too high.
Notes: Match property to purpose: low ρ to carry current, high ρ + high m.p. to make heat, low m.p. to make a fuse.

## Slide 9
SUPERCONDUCTORS
Superconductors
Resistance that drops to zero
• Zero resistance Below a very low critical temperature some materials lose all electrical resistance.
• No energy loss Current can flow with no heating and no energy wasted.
• Uses Powerful electromagnets in MRI scanners and maglev trains.
• The catch They must be kept extremely cold, which is expensive.
Notes: Superconductors: zero resistance below a critical temperature. Great for strong magnets, but cooling is the challenge.

## Slide 10
QUIZ 1
Check Your Understanding
4 questions • think before the answer reveals on the next slide

## Slide 11
QUIZ QUESTION
Q1 — Stretch the Wire
A wire is stretched so that its length doubles (its volume staying the same, so the area halves). Its new resistance becomes:
A
Half
B
The same
C
Double
D
Four times the original

## Slide 12
ANSWER REVEALED
Q1 — Stretch the Wire
A wire is stretched so that its length doubles (its volume staying the same, so the area halves). Its new resistance becomes:
A
Half
B
The same
C
Double
✓
Four times the original
WHY
R = ρL/A. Doubling the length doubles R, and halving the area doubles it again — together a factor of 4. A classic stretched-wire problem.

## Slide 13
QUIZ QUESTION
Q2 — Heater Element
Why is the heating element of an electric iron made of nichrome rather than copper?
A
Copper is too expensive
B
Nichrome has high resistivity and a high melting point, so it heats up without melting
C
Copper cannot carry current
D
Nichrome is a better conductor

## Slide 14
ANSWER REVEALED
Q2 — Heater Element
Why is the heating element of an electric iron made of nichrome rather than copper?
A
Copper is too expensive
✓
Nichrome has high resistivity and a high melting point, so it heats up without melting
C
Copper cannot carry current
D
Nichrome is a better conductor
WHY
A heater needs a wire that resists current strongly (to release heat) and survives high temperatures. Nichrome does both; copper conducts too well and would barely warm up.

## Slide 15
QUIZ QUESTION
Q3 — Thicker Wire
Replacing a wire with a thicker one of the same material and length will:
A
Increase its resistance
B
Decrease its resistance
C
Not change its resistance
D
Make it an insulator

## Slide 16
ANSWER REVEALED
Q3 — Thicker Wire
Replacing a wire with a thicker one of the same material and length will:
A
Increase its resistance
✓
Decrease its resistance
C
Not change its resistance
D
Make it an insulator
WHY
Resistance is inversely proportional to cross-sectional area. A thicker wire gives electrons more room to flow, lowering the resistance.

## Slide 17
QUIZ QUESTION
Q4 — Resistivity
Two wires, one copper and one iron, have the same length and thickness. They have different resistances because they differ in:
A
Length
B
Cross-sectional area
C
Resistivity (material)
D
Temperature only

## Slide 18
ANSWER REVEALED
Q4 — Resistivity
Two wires, one copper and one iron, have the same length and thickness. They have different resistances because they differ in:
A
Length
B
Cross-sectional area
✓
Resistivity (material)
D
Temperature only
WHY
With length and area equal, the only difference left is the material's resistivity ρ. Iron has a higher resistivity than copper, so the iron wire resists more.

## Slide 19
2
PART 2
Cells: EMF & Internal Resistance
Why a battery's voltage drops when it supplies current

## Slide 20
EMF
Electromotive Force (EMF)
The EMF of a cell is the energy it gives to each unit of charge — the p.d. across its terminals when no current is drawn.
EMF (E) = energy supplied / charge
• Measured in volts, like potential difference.
• It is the 'full' voltage of the cell on open circuit.
• Driving current through the cell's own materials uses up some of this energy.
Notes: EMF = total energy per charge from the cell. It is the open-circuit (no current) voltage.

## Slide 21
TERMINAL VOLTAGE
Terminal Voltage & Internal Resistance
When a cell supplies current, some voltage is lost inside it across its own internal resistance r.
V = E − I r
• E is the EMF, I the current, r the internal resistance.
• V is the terminal voltage available to the external circuit.
• The larger the current, the bigger the internal drop I r.
Notes: Terminal voltage V = E − Ir. This is why a car's headlights dim when the starter motor draws a big current.

## Slide 22
INTERNAL RESISTANCE
Internal Resistance of a Cell
The resistance inside the cell
• What it is The resistance of the cell's own electrolyte and electrodes.
• Effect It causes the terminal voltage to fall below the EMF when current flows.
• Open circuit With no current (I = 0), the terminal voltage equals the EMF.
• Old cells Internal resistance rises as a cell ages, so it delivers less voltage.
Notes: Internal resistance explains the gap between EMF and terminal voltage. At I = 0 the two are equal.

## Slide 23
WORKED EXAMPLE
Terminal Voltage
Problem. A cell of EMF 1.5 V and internal resistance 0.5 Ω drives a current of 0.6 A. Find its terminal voltage.
V = E − I r
V = 1.5 − (0.6 × 0.5)
V = 1.5 − 0.3 = 1.2 V
Answer: Terminal voltage V = 1.2 V
Notes: Substitute into V = E − Ir. The 0.3 V is 'lost' inside the cell across r.

## Slide 24
WRAP UP
Quick Recap
✓ Ohmic / non-ohmic — straight vs curved V–I graph
✓ Factors — R ∝ length, R ∝ 1/area, plus material & temperature
✓ Resistivity — R = ρL/A; ρ is a property of the material
✓ Material choice — copper to carry, nichrome/tungsten to heat
✓ EMF vs terminal V — V = E − I r
✓ Internal resistance — voltage lost inside the cell when current flows
Notes: Rapid recap; the stretched-wire and V = E − Ir ideas are the exam favourites.

## Slide 25
QUIZ 2
Final Check — Resistivity & Cells
5 questions • think before the answer reveals on the next slide

## Slide 26
QUIZ QUESTION
Q1 — Open Circuit
A voltmeter across a cell reads 1.5 V when no current is drawn, but only 1.3 V when the cell lights a bulb. The 1.5 V reading is the cell's:
A
Terminal voltage
B
Internal resistance
C
EMF
D
Power

## Slide 27
ANSWER REVEALED
Q1 — Open Circuit
A voltmeter across a cell reads 1.5 V when no current is drawn, but only 1.3 V when the cell lights a bulb. The 1.5 V reading is the cell's:
A
Terminal voltage
B
Internal resistance
✓
EMF
D
Power
WHY
With no current there is no internal voltage drop, so the terminal voltage equals the EMF (1.5 V). Once current flows, I r is lost inside and the terminal voltage falls to 1.3 V.

## Slide 28
QUIZ QUESTION
Q2 — Find r
Using the cell above (EMF 1.5 V, terminal voltage 1.3 V when the current is 0.5 A), the internal resistance is:
A
0.2 Ω
B
0.4 Ω
C
2.6 Ω
D
0.5 Ω

## Slide 29
ANSWER REVEALED
Q2 — Find r
Using the cell above (EMF 1.5 V, terminal voltage 1.3 V when the current is 0.5 A), the internal resistance is:
A
0.2 Ω
✓
0.4 Ω
C
2.6 Ω
D
0.5 Ω
WHY
The lost voltage is E − V = 1.5 − 1.3 = 0.2 V. Since this equals I r, r = 0.2 / 0.5 = 0.4 Ω.

## Slide 30
QUIZ QUESTION
Q3 — Longer Wire
A uniform wire has resistance 6 Ω. A piece one third of its length would have resistance:
A
18 Ω
B
6 Ω
C
3 Ω
D
2 Ω

## Slide 31
ANSWER REVEALED
Q3 — Longer Wire
A uniform wire has resistance 6 Ω. A piece one third of its length would have resistance:
A
18 Ω
B
6 Ω
C
3 Ω
✓
2 Ω
WHY
Resistance is proportional to length. One third of the length has one third of the resistance: 6 / 3 = 2 Ω.

## Slide 32
QUIZ QUESTION
Q4 — Same Material
Which property is the SAME for a thick copper wire and a thin copper wire?
A
Resistance
B
Cross-sectional area
C
Resistivity
D
Current they carry

## Slide 33
ANSWER REVEALED
Q4 — Same Material
Which property is the SAME for a thick copper wire and a thin copper wire?
A
Resistance
B
Cross-sectional area
✓
Resistivity
D
Current they carry
WHY
Resistivity depends only on the material (and temperature), so both copper wires share it. Their resistances differ because their areas differ.

## Slide 34
QUIZ QUESTION
Q5 — Why Dim?
A car's headlights dim for a moment when the engine is started. This is because the starter motor:
A
Increases the EMF
B
Draws a large current, so the internal drop I r lowers the terminal voltage
C
Cools the battery
D
Breaks Ohm's law

## Slide 35
ANSWER REVEALED
Q5 — Why Dim?
A car's headlights dim for a moment when the engine is started. This is because the starter motor:
A
Increases the EMF
✓
Draws a large current, so the internal drop I r lowers the terminal voltage
C
Cools the battery
D
Breaks Ohm's law
WHY
The starter draws a huge current, so the voltage lost inside the battery (I r) jumps. The terminal voltage falls, momentarily dimming the lights.

## Slide 36
Inside Every Wire and Cell
Resistivity shapes the wire; internal resistance shapes the cell — together they decide what a circuit can do.