## Slide 1
MAGNETISM
Magnetism — 2
Making a magnet • Electromagnets • Care & storage • Losing magnetism

## Slide 2
INTRODUCTION
Learning Objectives
2
1
Describe ways of making a magnet
2
Explain the single-touch (stroking) method
3
Describe an electromagnet and how to make one stronger
4
Tell temporary magnets apart from permanent magnets
5
State how magnets should be stored and cared for
6
List the ways a magnet can lose its magnetism
Notes: Open by previewing these objectives so students know what they should be able to do by the end of the session.

## Slide 3
1
PART 1
Making Magnets
Turning steel and iron into magnets
3

## Slide 4
HOW TO MAGNETISE
Ways to Make a Magnet
4
Single touch
Stroke a steel bar again and again in one direction with one pole of a magnet.
Double touch
Stroke the bar from the middle outwards using two unlike poles together.
By induction
Simply bringing a magnet near a piece of iron makes the iron a temporary magnet.
By electricity
Pass an electric current through a coil wound around the bar — this makes an electromagnet.
Notes: Introduce the four ways to magnetise. Single touch is the one to know in detail. Induction is temporary; the electrical method is the strongest and is used in electromagnets.

## Slide 5
SINGLE TOUCH
The Single-Touch Method
5
Stroke in one direction, again and again
Stroke one way
• Place the steel bar flat on the table.
• Stroke it from one end to the other with one pole of a magnet.
• Lift the magnet high at the end of each stroke and repeat many times in the same direction.
• The bar becomes a magnet; the end where the stroking pole leaves it gets the opposite polarity.
Notes: Demonstrate the stroking action. Two rules: always stroke in the SAME direction, and lift the pole well clear between strokes. The finishing end takes the polarity opposite to the stroking pole.

## Slide 6
ELECTROMAGNET
Making an Electromagnet
6
Current in the coil magnetises the iron core
Coil + iron core
• Wind insulated copper wire into a coil around a soft-iron core.
• Connect the ends of the coil to a cell through a switch.
• When current flows, the iron core becomes a strong magnet.
• Switch the current off and the magnetism almost completely disappears — it is a temporary magnet.
Notes: Build the electromagnet step by step. The headline idea: its magnetism can be switched on and off with the current — that is what makes it so useful.

## Slide 7
STRONGER
Making an Electromagnet Stronger
7
More turns
Winding more turns of wire on the coil makes the electromagnet stronger.
More current
Increasing the current through the coil increases its strength.
A soft-iron core
A soft-iron core becomes strongly magnetic and boosts the field.
Switchable
Its magnetism can be turned on and off and even reversed — a permanent magnet cannot do this.
Notes: Three ways to strengthen: more turns, more current, soft-iron core. End on the big advantage — it can be switched and reversed.

## Slide 8
TEMPORARY VS PERMANENT
Temporary and Permanent Magnets
8
Temporary magnets
Made of soft iron; magnetic only while the current flows. Used in electromagnets.
Permanent magnets
Made of steel; keep their magnetism for a long time. Used in compasses and fridge magnets.
Soft iron
Is easy to magnetise and easy to demagnetise.
Steel
Is harder to magnetise but holds its magnetism well.
Notes: Contrast soft iron (temporary, for electromagnets) with steel (permanent). Tie the choice of material to the job the magnet must do.

## Slide 9
INDUCTION
Magnetism by Induction
9
A magnet makes more magnets
• No touching needed Simply bringing a magnet near a piece of iron turns the iron into a temporary magnet.
• Chains of pins A nail clinging to a magnet can itself pick up more nails, which hang in a chain.
• It is temporary Take the magnet away and the induced magnetism almost completely disappears.
• Why attraction works A magnet first induces magnetism in the iron, and that is what lets it then pull the iron in.
Notes: Demonstrate induction with a chain of pins hanging from one magnet. The key idea: induction comes first, and that is the real reason a magnet can attract a piece of iron.

## Slide 10
QUIZ 1
Quick Check — Making Magnets
4 questions • think before the answer reveals on the next slide
10

## Slide 11
QUIZ QUESTION
Q1 - Method
11
In the single-touch method, the steel bar is stroked:
A
In both directions
B
In one direction only
C
Very gently once
D
Without a magnet

## Slide 12
QUIZ QUESTION
Q1 - Method
12
In the single-touch method, the steel bar is stroked:
A
In both directions
B
In one direction only
✓
C
Very gently once
D
Without a magnet
Why In single touch you stroke the bar repeatedly in the same direction with one pole, lifting the magnet clear between strokes.

## Slide 13
QUIZ QUESTION
Q2 - Electromagnet
13
An electromagnet is made by passing current through a coil wound on a core of:
A
Steel
B
Soft iron
C
Copper
D
Plastic

## Slide 14
QUIZ QUESTION
Q2 - Electromagnet
14
An electromagnet is made by passing current through a coil wound on a core of:
A
Steel
B
Soft iron
✓
C
Copper
D
Plastic
Why A soft-iron core becomes strongly magnetic when current flows and loses it when the current stops, making a good electromagnet.

## Slide 15
QUIZ QUESTION
Q3 - Strength
15
Which change makes an electromagnet stronger?
A
Fewer turns of wire
B
Less current
C
More turns of wire
D
A plastic core

## Slide 16
QUIZ QUESTION
Q3 - Strength
16
Which change makes an electromagnet stronger?
A
Fewer turns of wire
B
Less current
C
More turns of wire
✓
D
A plastic core
Why More turns of wire (and more current, and a soft-iron core) make an electromagnet stronger.

## Slide 17
QUIZ QUESTION
Q4 - Type
17
A permanent magnet is usually made of:
A
Soft iron
B
Steel
C
Copper
D
Aluminium

## Slide 18
QUIZ QUESTION
Q4 - Type
18
A permanent magnet is usually made of:
A
Soft iron
B
Steel
✓
C
Copper
D
Aluminium
Why Steel is hard to magnetise but holds its magnetism for a long time, so it is used to make permanent magnets.

## Slide 19
2
PART 2
Uses, Care & Demagnetisation
Where electromagnets help, and how magnetism is kept or lost
19

## Slide 20
USES
Uses of Electromagnets
20
Lifting cranes
Powerful electromagnets on cranes lift heavy iron and steel scrap, then drop it by switching off.
Electric bell
An electromagnet makes the hammer strike the gong again and again.
Machines
Electromagnets are used in electric motors, loudspeakers, telephones and many devices.
Separating metals
They pull magnetic metals out of mixed waste for recycling.
Notes: Connect electromagnets to real machines. The crane (switch on to lift, off to drop) best shows why a switchable magnet is so useful.

## Slide 21
CARE
Caring For and Storing Magnets
21
Looking after magnets
• Store in pairs Keep bar magnets in pairs with unlike poles together.
• Use keepers Place soft-iron pieces (keepers) across the ends to preserve their magnetism.
• Keep them safe Do not drop, hammer or heat magnets — this weakens them.
• Keep apart Store magnets away from watches, mobile phones and other magnets.
Notes: Explain why magnets need care. Keepers give the field a closed path and stop the magnet weakening. Heat, shock and stray fields are the enemies.

## Slide 22
DEMAGNETISATION
How a Magnet Loses Its Magnetism
22
A magnet can lose its magnetism if it is treated roughly or heated — this is called demagnetisation.
• Heating a magnet strongly and then cooling it makes it lose its magnetism.
• Hammering or dropping a magnet again and again weakens it.
• Placing it in a coil carrying alternating current (AC) removes its magnetism.
• Careless storage near other magnets also makes a magnet weaker over time.
Notes: List the three deliberate ways to demagnetise — heating, rough handling, and an AC coil — and tie them back to the care rules from the previous slide.

## Slide 23
PERMANENT VS TEMPORARY
Choosing the Right Magnet
23
Need it to last?
Use a permanent (steel) magnet — for a compass or a fridge magnet.
Need to switch it?
Use an electromagnet — for a crane or an electric bell.
Need it strong?
An electromagnet can be made very strong with more turns and more current.
Keep it safe
Either kind weakens with heat, shock and careless storage, so handle with care.
Notes: Wrap the chapter by matching the magnet to the job: permanent for lasting magnetism, electromagnet for switchable strength.

## Slide 24
KEEPERS
Why Magnets Need Keepers
24
Storing bar magnets safely
• Free poles weaken Left on their own, the free poles of a magnet slowly lose their strength.
• Store in pairs Place two bar magnets side by side with unlike poles next to each other.
• Add soft-iron keepers Lay small soft-iron bars across the ends to link the poles together.
• A complete loop The keepers give the magnetism a closed path, so the magnets stay strong for much longer.
Notes: Explain how keepers work: by completing the magnetic loop they stop the poles weakening. This ties the storage rule back to the idea of field lines forming closed loops.

## Slide 25
WRAP UP
Quick Recap
25
✓ Making magnets — single touch, double touch, induction, electricity
✓ Single touch — stroke one way, lift between strokes
✓ Electromagnet — coil + soft-iron core; magnetism while current flows
✓ Stronger — more turns, more current, soft-iron core
✓ Care — store in pairs with keepers; avoid heat, shock, stray fields
✓ Demagnetise — heating, hammering/dropping, an AC coil
Notes: Rapid recap. Cold-call students for the ways to make a magnet and the ways to demagnetise one.

## Slide 26
QUIZ 2
Final Check — Using & Losing Magnetism
4 questions • think before the answer reveals on the next slide
26

## Slide 27
QUIZ QUESTION
Q1 - Uses
27
A crane in a scrapyard lifts heavy iron using a:
A
Permanent magnet
B
Wooden hook
C
An electromagnet
D
A plastic clamp

## Slide 28
QUIZ QUESTION
Q1 - Uses
28
A crane in a scrapyard lifts heavy iron using a:
A
Permanent magnet
B
Wooden hook
C
An electromagnet
✓
D
A plastic clamp
Why A crane uses an electromagnet: switch the current on to lift the iron, and off to drop it. A permanent magnet could not let go.

## Slide 29
QUIZ QUESTION
Q2 - Care
29
The soft-iron pieces placed across the ends of stored magnets are called:
A
Poles
B
Keepers
C
Cores
D
Coils

## Slide 30
QUIZ QUESTION
Q2 - Care
30
The soft-iron pieces placed across the ends of stored magnets are called:
A
Poles
B
Keepers
✓
C
Cores
D
Coils
Why Keepers are soft-iron pieces placed across the poles of stored magnets to preserve their magnetism.

## Slide 31
QUIZ QUESTION
Q3 - Demagnetise
31
Which of these will make a magnet lose its magnetism?
A
Storing it with keepers
B
Strongly heating it
C
Keeping it dry
D
Handling it gently

## Slide 32
QUIZ QUESTION
Q3 - Demagnetise
32
Which of these will make a magnet lose its magnetism?
A
Storing it with keepers
B
Strongly heating it
✓
C
Keeping it dry
D
Handling it gently
Why Strong heating, repeated hammering or dropping, and an AC coil all destroy magnetism. Careful storage with keepers preserves it.

## Slide 33
QUIZ QUESTION
Q4 - Electromagnet
33
The magnetism of an electromagnet lasts:
A
For ever
B
Only while current flows
C
Only at night
D
Only when it is hot

## Slide 34
QUIZ QUESTION
Q4 - Electromagnet
34
The magnetism of an electromagnet lasts:
A
For ever
B
Only while current flows
✓
C
Only at night
D
Only when it is hot
Why An electromagnet is a temporary magnet — it is magnetic only while current flows through its coil, and loses it when switched off.

## Slide 35
Magnets On Demand
From a stroked steel bar to a switchable electromagnet, we can make, use and even switch off magnetism whenever we need it.