## Slide 1
STD 10 • SCIENCE PART 1 • ELECTRICITY
Effects of Electric Current — 1
Energy transfer in a circuit • Heating effect • Magnetic effect • Right-hand thumb rule

## Slide 2
INTRODUCTION
Learning Objectives
1
Explain how electrical energy is transferred and used up in a circuit
2
State Joule's law of heating and use H = I²Rt
3
Describe everyday uses of the heating effect of current
4
State Oersted's discovery of the magnetic effect of current
5
Apply the right-hand thumb rule to a straight current-carrying conductor
6
Describe the magnetic field pattern of a straight wire
Notes: Open by previewing these objectives so students know what they should be able to do by the end of the session.

## Slide 3
1
PART 1
Energy Transfer and the Heating Effect
How electrical work becomes heat

## Slide 4
ENERGY TRANSFER
Energy Transfer in an Electric Circuit
From battery to heat
• A cell (or battery) does work to push charge around a circuit; this electrical energy is converted into other forms by the components in the circuit.
• The work done in moving a charge Q through a potential difference V is W = VQ; since Q = It, the work done in time t is W = VIt.
• In a purely resistive component (like a heater coil or a bulb filament), all of this electrical energy is converted into heat.
• This conversion of electrical energy into heat because of the resistance in the circuit is called the heating effect of electric current.
Notes: Link back to V = W/Q from the current-electricity chapter; this is the same relation used to derive Joule's law.

## Slide 5
JOULE'S LAW
Joule's Law of Heating
Using Ohm's law (V = IR) in W = VIt gives the heat produced in a resistor carrying a current for a given time.
H = I² R t
• The heat produced is directly proportional to the square of the current.
• The heat produced is directly proportional to the resistance.
• The heat produced is directly proportional to the time for which the current flows.
• H is in joules when I is in amperes, R in ohms and t in seconds.
Notes: Emphasise the squared dependence on current — doubling the current quadruples the heat produced, not just doubles it.

## Slide 6
WORKED EXAMPLE
Heat Produced in a Resistor
Problem. A current of 2 A flows through a resistor of 10 Ω for 5 minutes. Calculate the heat produced.
H = I² R t
t = 5 x 60 = 300 s
H = (2)² x 10 x 300
Answer: H = 12000 J = 12 kJ
Notes: Remind students to convert time to seconds before substituting — a very common slip.

## Slide 7
USES
Everyday Uses of the Heating Effect
Electric heater / iron
A coil of high-resistance wire (nichrome) glows and produces heat when current flows through it, used for room heaters, electric irons and geysers.
Incandescent bulb
A thin tungsten filament heats up so much that it glows white-hot and emits light; tungsten is used because it has a very high melting point.
Electric fuse
A thin wire of low melting point is placed in series in a circuit; if the current becomes too large, the fuse wire heats up, melts and breaks the circuit, protecting the appliance.
Soldering iron
A high-resistance heating element converts electrical energy to heat to melt solder for joining wires and components.
Notes: Ask students to name the common factor in all four devices — each deliberately uses a high-resistance element to maximise I²Rt heating.

## Slide 8
QUIZ 1
Check — Energy Transfer & Heating
4 questions • think before the answer reveals on the next slide

## Slide 9
QUIZ QUESTION
Q1 — Energy transfer
The work done in moving a charge Q through a potential difference V is given by:
A
W = V / Q
B
W = VQ
C
W = Q / V
D
W = V + Q

## Slide 10
ANSWER REVEALED
Q1 — Energy transfer
The work done in moving a charge Q through a potential difference V is given by:
A
W = V / Q
✓
W = VQ
C
W = Q / V
D
W = V + Q
WHY
Potential difference is defined as work done per unit charge, so W = VQ (and since Q = It, W = VIt).

## Slide 11
QUIZ QUESTION
Q2 — Joule's law
According to Joule's law of heating, the heat produced in a resistor is proportional to:
A
I and R only
B
I², R and t
C
I and t only
D
R² and I

## Slide 12
ANSWER REVEALED
Q2 — Joule's law
According to Joule's law of heating, the heat produced in a resistor is proportional to:
A
I and R only
✓
I², R and t
C
I and t only
D
R² and I
WHY
H = I²Rt — heat depends on the square of the current, and directly on resistance and time.

## Slide 13
QUIZ QUESTION
Q3 — Numerical
A current of 3 A flows through a 4 Ω resistor for 10 s. The heat produced is:
A
120 J
B
360 J
C
40 J
D
12 J

## Slide 14
ANSWER REVEALED
Q3 — Numerical
A current of 3 A flows through a 4 Ω resistor for 10 s. The heat produced is:
A
120 J
✓
360 J
C
40 J
D
12 J
WHY
H = I²Rt = (3)² x 4 x 10 = 9 x 4 x 10 = 360 J.

## Slide 15
QUIZ QUESTION
Q4 — Fuse
An electric fuse protects a circuit because its wire:
A
has a very high melting point so it never melts
B
has a low melting point and melts to break the circuit when current is too high
C
is a perfect conductor
D
increases the current when it gets hot

## Slide 16
ANSWER REVEALED
Q4 — Fuse
An electric fuse protects a circuit because its wire:
A
has a very high melting point so it never melts
✓
has a low melting point and melts to break the circuit when current is too high
C
is a perfect conductor
D
increases the current when it gets hot
WHY
A fuse wire is deliberately chosen to melt (via I²Rt heating) and break the circuit before the current can damage the appliance or wiring.

## Slide 17
2
PART 2
The Magnetic Effect of Electric Current
Oersted's discovery and the right-hand thumb rule

## Slide 18
OERSTED'S EXPERIMENT
Discovery of the Magnetic Effect
• In 1820, Hans Christian Oersted found that a compass needle placed near a current-carrying wire is deflected.
• The needle deflects only when current flows in the wire, and returns to normal when the current is switched off.
• Reversing the direction of the current reverses the direction of the deflection.
• This showed that an electric current produces a magnetic field around itself — the magnetic effect of electric current, the basis of electromagnetism.
Notes: This experiment is historically important: it was the first evidence linking electricity and magnetism, which later led to Maxwell's unified theory.

## Slide 19
STRAIGHT CONDUCTOR
Field Around a Straight Current-Carrying Wire
Concentric field circles
• A long straight wire carrying current produces a magnetic field whose field lines are concentric circles centred on the wire, lying in a plane perpendicular to it.
• The field is stronger closer to the wire and weaker farther away — the circles are more crowded near the wire.
• Reversing the current reverses the direction of the field lines (clockwise becomes anticlockwise, viewed from a fixed end).
Notes: Have students trace the field-line circles with their finger around a pencil representing the wire.

## Slide 20
RIGHT-HAND THUMB RULE
Finding the Direction of the Field
Thumb = current, curl = field
• Maxwell's right-hand thumb rule gives a quick way to find the direction of the magnetic field around a straight conductor.
• Hold the current-carrying conductor in your right hand with the thumb pointing in the direction of the conventional current.
• Your curled fingers then point in the direction of the magnetic field lines around the wire.
• By convention, a dot (⊙) shows the field or current coming out of the page, and a cross (⊗) shows it going into the page.
Notes: Demonstrate physically with your own hand and the diagram side by side; this rule is used repeatedly through the rest of the chapter.

## Slide 21
WRAP UP
Quick Recap
✓ Heating effect — Electrical energy converts to heat in a resistor: H = I²Rt.
✓ Uses — Heaters, bulb filaments, fuses and soldering irons all use the heating effect.
✓ Oersted's experiment — A current-carrying wire deflects a nearby compass needle — proof of the magnetic effect.
✓ Straight wire field — Concentric circular field lines around the wire.
✓ Right-hand thumb rule — Thumb along the current, curled fingers show the field direction.
Notes: Ask a student to physically demonstrate the right-hand thumb rule for the class.

## Slide 22
QUIZ 2
Final Check — Magnetic Effect
4 questions • think before the answer reveals on the next slide

## Slide 23
QUIZ QUESTION
Q1 — Oersted
Oersted's experiment showed that a current-carrying wire:
A
repels a nearby wire
B
deflects a nearby compass needle
C
heats up a nearby magnet
D
has no effect on a compass

## Slide 24
ANSWER REVEALED
Q1 — Oersted
Oersted's experiment showed that a current-carrying wire:
A
repels a nearby wire
✓
deflects a nearby compass needle
C
heats up a nearby magnet
D
has no effect on a compass
WHY
The deflection, seen only while current flows, proved that current produces a magnetic field.

## Slide 25
QUIZ QUESTION
Q2 — Field pattern
The magnetic field lines around a long straight current-carrying wire are:
A
straight lines parallel to the wire
B
concentric circles centred on the wire
C
radial lines pointing away from the wire
D
randomly scattered

## Slide 26
ANSWER REVEALED
Q2 — Field pattern
The magnetic field lines around a long straight current-carrying wire are:
A
straight lines parallel to the wire
✓
concentric circles centred on the wire
C
radial lines pointing away from the wire
D
randomly scattered
WHY
The field forms circles in a plane perpendicular to the wire, crowded closer to the wire where the field is stronger.

## Slide 27
QUIZ QUESTION
Q3 — Right-hand thumb rule
In the right-hand thumb rule, the thumb points along the:
A
magnetic field
B
current
C
force on the wire
D
normal to the wire

## Slide 28
ANSWER REVEALED
Q3 — Right-hand thumb rule
In the right-hand thumb rule, the thumb points along the:
A
magnetic field
✓
current
C
force on the wire
D
normal to the wire
WHY
Thumb = direction of conventional current; curled fingers = direction of the magnetic field.

## Slide 29
QUIZ QUESTION
Q4 — Reversal
If the current in a straight wire is reversed, the magnetic field around it:
A
disappears completely
B
also reverses direction
C
stays exactly the same
D
becomes twice as strong

## Slide 30
ANSWER REVEALED
Q4 — Reversal
If the current in a straight wire is reversed, the magnetic field around it:
A
disappears completely
✓
also reverses direction
C
stays exactly the same
D
becomes twice as strong
WHY
Reversing the thumb direction in the right-hand rule reverses the curl of the fingers, so the field direction flips too.

## Slide 31
Current in Motion, Heat and Magnetism
The same flowing charge that warms a heater coil also conjures a magnetic field around every wire — two effects, one current.