## Slide 1
STD 9 • SCIENCE & TECHNOLOGY • ELECTRICITY
Current Electricity — 2
Resistance and resistivity • Resistors in series and parallel • Domestic circuits and safety

## Slide 2
INTRODUCTION
Learning Objectives
1
Define resistance and resistivity of a conductor
2
State the factors on which the resistance of a wire depends
3
Derive and use the formula for resistors in series
4
Derive and use the formula for resistors in parallel
5
Describe domestic electrical connections
6
State the safety precautions to be taken while using electricity
Notes: Open by previewing these objectives so students know what they should be able to do by the end of the session.

## Slide 3
1
PART 1
Resistance and Resistivity
What opposes the current, and what it depends on

## Slide 4
RESISTANCE
Resistance of a Conductor
The resistance of a conductor is the opposition it offers to the flow of electric current through it.
R = V / I
• The SI unit of resistance is the ohm (Ω).
• Resistance arises because the drifting electrons collide with the atoms of the conductor, losing energy as heat.
• A good conductor has low resistance; an insulator has very high resistance.
Notes: Connect to Ohm's law from the previous session: R = V/I is the same relation rearranged.

## Slide 5
FACTORS
Factors Affecting the Resistance of a Wire
Length, thickness, material and temperature
• Length: the resistance of a wire is directly proportional to its length — a longer wire has more resistance.
• Area of cross-section: the resistance is inversely proportional to the area of cross-section — a thicker wire has less resistance.
• Material: different materials have different resistances for the same dimensions, described by a property called resistivity.
• Temperature: for most conductors the resistance increases as the temperature rises.
Notes: Give the everyday link: thin, long wires (like a heater coil) have high resistance; thick, short copper wires have low resistance.

## Slide 6
RESISTIVITY
Resistivity (Specific Resistance)
Combining the effects of length (l) and area of cross-section (A) gives the resistance in terms of a material constant called resistivity (ρ).
R = ρ l / A
• Resistivity is the resistance of a wire of that material of unit length and unit area of cross-section.
• Its SI unit is the ohm-metre (Ω·m); it depends only on the material (and temperature), not on the wire's dimensions.
• Metals such as silver and copper have very low resistivity (good conductors); alloys such as nichrome have high resistivity (used in heating elements).
Notes: Distinguish resistance (depends on the specific wire) from resistivity (a property of the material).

## Slide 7
QUIZ 1
Check — Resistance & Resistivity
4 questions • think before the answer reveals on the next slide

## Slide 8
QUIZ QUESTION
Q1 — Resistance
The resistance of a conductor is the:
A
ease with which current flows
B
opposition it offers to the flow of current
C
charge stored in it
D
potential difference across it

## Slide 9
ANSWER REVEALED
Q1 — Resistance
The resistance of a conductor is the:
A
ease with which current flows
✓
opposition it offers to the flow of current
C
charge stored in it
D
potential difference across it
WHY
Resistance opposes current; it arises from collisions of drifting electrons with the conductor's atoms.

## Slide 10
QUIZ QUESTION
Q2 — Length
If the length of a wire is doubled (keeping everything else the same), its resistance:
A
halves
B
doubles
C
stays the same
D
becomes four times

## Slide 11
ANSWER REVEALED
Q2 — Length
If the length of a wire is doubled (keeping everything else the same), its resistance:
A
halves
✓
doubles
C
stays the same
D
becomes four times
WHY
Resistance is directly proportional to length (R = ρl/A), so doubling the length doubles the resistance.

## Slide 12
QUIZ QUESTION
Q3 — Thickness
A thicker wire (larger area of cross-section) of the same material and length has:
A
more resistance
B
less resistance
C
the same resistance
D
zero resistance

## Slide 13
ANSWER REVEALED
Q3 — Thickness
A thicker wire (larger area of cross-section) of the same material and length has:
A
more resistance
✓
less resistance
C
the same resistance
D
zero resistance
WHY
Resistance is inversely proportional to the area of cross-section, so a thicker wire offers less resistance.

## Slide 14
QUIZ QUESTION
Q4 — Resistivity
The resistivity of a material depends on:
A
the length of the wire
B
the thickness of the wire
C
the material and its temperature
D
the current through it

## Slide 15
ANSWER REVEALED
Q4 — Resistivity
The resistivity of a material depends on:
A
the length of the wire
B
the thickness of the wire
✓
the material and its temperature
D
the current through it
WHY
Resistivity is a property of the material (and its temperature); it does not depend on the wire's dimensions.

## Slide 16
2
PART 2
Combinations of Resistors and Domestic Circuits
Adding resistances, and using electricity safely at home

## Slide 17
SERIES
Resistors in Series
When resistors are joined end to end so that the same current flows through each, they are said to be connected in series.
Rs = R₁ + R₂ + R₃ + ...
• The same current flows through every resistor in a series combination.
• The total potential difference is shared among the resistors and equals the sum of the individual potential differences.
• The equivalent (total) resistance is larger than the largest individual resistance.
Notes: Everyday link: old decorative light strings are in series, so if one bulb fails the whole string goes off.

## Slide 18
PARALLEL
Resistors in Parallel
Same voltage, shared current
• When resistors are connected between the same two points so that the same potential difference acts across each, they are in parallel.
• The potential difference is the same across every resistor, while the main current is shared among the branches.
• The reciprocal of the equivalent resistance equals the sum of the reciprocals of the individual resistances: 1/Rp = 1/R₁ + 1/R₂ + 1/R₃ + ...
• The equivalent resistance of a parallel combination is smaller than the smallest individual resistance.
Notes: Household appliances are wired in parallel so each gets the full mains voltage and can be switched independently.

## Slide 19
WORKED EXAMPLE
Series and Parallel Combinations
Problem. Two resistors of 6 Ω and 3 Ω are connected (i) in series and (ii) in parallel. Find the equivalent resistance in each case.
Series: Rs = R₁ + R₂ = 6 + 3 = 9 Ω
Parallel: 1/Rp = 1/6 + 1/3 = 1/6 + 2/6 = 3/6 = 1/2
Rp = 2 Ω
Answer: Series = 9 Ω; Parallel = 2 Ω
Notes: Note the parallel result (2 Ω) is less than the smaller resistor (3 Ω) — a good check on the arithmetic.

## Slide 20
DOMESTIC CIRCUITS & SAFETY
Domestic Connections and Safety
• Parallel wiring at home Appliances in a house are connected in parallel across the live and neutral wires, so each receives the full supply voltage and works independently.
• Live, neutral and earth The supply reaches a house through the live and neutral wires; a separate earth wire safely carries away leakage current.
• Fuse and MCB A fuse or a miniature circuit breaker (MCB) is placed in the live wire; it breaks the circuit if the current becomes dangerously large.
• Safety precautions Never touch switches or appliances with wet hands, use properly earthed three-pin plugs for heavy appliances, and use wires and fuses of the correct rating.
Notes: Tie the fuse action back to the heating effect of current: an overload heats and melts the fuse wire, breaking the circuit.

## Slide 21
WRAP UP
Quick Recap
✓ Resistance — Opposition to current, R = V/I, unit ohm.
✓ Factors — R increases with length, decreases with thickness; depends on material and temperature.
✓ Resistivity — R = ρl/A; ρ is a material property, unit ohm-metre.
✓ Series — Same current; Rs = R₁ + R₂ + ... (larger than any one).
✓ Parallel — Same voltage; 1/Rp = 1/R₁ + 1/R₂ + ... (smaller than any one).
✓ Domestic safety — Parallel wiring, earthing, fuse/MCB in the live wire, correct ratings.
Notes: Ask students to predict whether combining resistors in parallel raises or lowers the total resistance, and why.

## Slide 22
QUIZ 2
Final Check — Combinations & Domestic Circuits
4 questions • think before the answer reveals on the next slide

## Slide 23
QUIZ QUESTION
Q1 — Series
Three resistors of 2 Ω, 3 Ω and 5 Ω are connected in series. Their equivalent resistance is:
A
10 Ω
B
0.97 Ω
C
3.3 Ω
D
1 Ω

## Slide 24
ANSWER REVEALED
Q1 — Series
Three resistors of 2 Ω, 3 Ω and 5 Ω are connected in series. Their equivalent resistance is:
✓
10 Ω
B
0.97 Ω
C
3.3 Ω
D
1 Ω
WHY
In series, Rs = R₁ + R₂ + R₃ = 2 + 3 + 5 = 10 Ω.

## Slide 25
QUIZ QUESTION
Q2 — Parallel
Two 4 Ω resistors are connected in parallel. Their equivalent resistance is:
A
8 Ω
B
4 Ω
C
2 Ω
D
0.5 Ω

## Slide 26
ANSWER REVEALED
Q2 — Parallel
Two 4 Ω resistors are connected in parallel. Their equivalent resistance is:
A
8 Ω
B
4 Ω
✓
2 Ω
D
0.5 Ω
WHY
1/Rp = 1/4 + 1/4 = 1/2, so Rp = 2 Ω — for two equal resistors in parallel, the result is half of one.

## Slide 27
QUIZ QUESTION
Q3 — Home wiring
Electrical appliances in a house are connected in parallel mainly so that:
A
they use less current
B
each gets the full supply voltage and can be operated independently
C
the wiring is cheaper
D
the fuse never blows

## Slide 28
ANSWER REVEALED
Q3 — Home wiring
Electrical appliances in a house are connected in parallel mainly so that:
A
they use less current
✓
each gets the full supply voltage and can be operated independently
C
the wiring is cheaper
D
the fuse never blows
WHY
Parallel wiring gives every appliance the full mains voltage and lets each be switched on or off without affecting the others.

## Slide 29
QUIZ QUESTION
Q4 — Safety
In domestic wiring, the fuse or MCB is connected in the ___ wire.
A
earth
B
neutral
C
live
D
any

## Slide 30
ANSWER REVEALED
Q4 — Safety
In domestic wiring, the fuse or MCB is connected in the ___ wire.
A
earth
B
neutral
✓
live
D
any
WHY
The fuse/MCB is placed in the live wire so that, when it breaks, the appliance is disconnected from the live supply and is safe to handle.

## Slide 31
Controlling the Current
Resistance and resistivity decide how much current flows; series and parallel rules let us combine resistors, and safe domestic wiring puts it all to everyday use.