## Slide 1
ICSE • CLASS 10 • MAGNETISM
Magnetic Effect of Current
Oersted's experiment • Field of a wire, loop & solenoid • The electromagnet

## Slide 2
INTRODUCTION
Learning Objectives
1
Describe Oersted's experiment linking current and magnetism
2
Draw the magnetic field around a straight current-carrying wire
3
Use the right-hand thumb rule for field direction
4
Describe the field of a current loop and a solenoid
5
Explain how an electromagnet is made and strengthened
6
Compare an electromagnet with a permanent magnet
Notes: Open by previewing these objectives so students know what they should be able to do by the end of the session.

## Slide 3
1
PART 1
Current Makes Magnetism
Oersted's discovery and the field of a wire

## Slide 4
OERSTED
Oersted's Experiment
Electricity and magnetism are linked
• The discovery A compass needle near a wire deflects when a current flows through the wire.
• What it shows An electric current produces a magnetic field around it.
• Reverse the current The needle deflects the other way — the field direction reverses too.
• No current, no effect Switch the current off and the needle returns to north.
Notes: Oersted's chance discovery: current creates magnetism. The needle deflection and its reversal are the key observations.

## Slide 5
STRAIGHT WIRE
Field Around a Straight Wire
Right-hand thumb rule gives the direction
Circular field lines
• The magnetic field lines form concentric circles around the wire.
• The field is stronger close to the wire and weakens with distance.
• Right-hand thumb rule: thumb points along the current, curled fingers show the field direction.
• Reversing the current reverses the direction of the field lines.
Notes: Field = concentric circles. Demonstrate the right-hand rule with your own hand; reversal flips the circles.

## Slide 6
CURRENT LOOP
Field Due to a Circular Loop
Bending the wire concentrates the field
• Each part adds up Every bit of the loop circles a field; inside the loop they all add together.
• Straight through the centre The field at the centre is perpendicular to the plane of the loop.
• Like a tiny magnet One face of the loop acts as a north pole, the other as a south pole.
• More turns, stronger Many turns side by side make the field much stronger.
Notes: A loop concentrates the field through its centre, behaving like a small magnet — the stepping stone to the solenoid.

## Slide 7
SOLENOID
The Solenoid
Reverse the current to swap the poles
A coil that acts like a bar magnet
• A solenoid is a long coil of many turns of insulated wire.
• When current flows, its field is just like that of a bar magnet, with a N and a S pole.
• The field inside is strong and nearly uniform.
• Reversing the current swaps the north and south poles.
Notes: Solenoid = many loops = bar-magnet field. Strong uniform field inside; poles reverse with the current.

## Slide 8
ELECTROMAGNET
Making an Electromagnet
Put a soft-iron core inside a solenoid and it becomes a powerful, switchable magnet — an electromagnet.
• The soft-iron core greatly increases the strength of the field.
• Stronger with more turns, more current, and a soft-iron core.
• It is a magnet only while the current flows.
Notes: Electromagnet = solenoid + soft-iron core. Strength depends on turns, current and the core.

## Slide 9
STRENGTH
What Makes an Electromagnet Stronger
Current, turns and core
• More current A larger current through the coil gives a stronger magnetic field.
• More turns Packing in more turns of wire increases the field.
• Soft-iron core A soft-iron core multiplies the strength many times over.
• Shorter / closer Bringing the turns closer together concentrates the field.
Notes: The three controllable factors: current, number of turns and the core. These are common one-mark answers.

## Slide 10
ELECTRO VS PERMANENT
Electromagnet vs Permanent Magnet
Switchable
An electromagnet can be turned on and off; a permanent magnet is always magnetic.
Adjustable strength
Its strength can be changed by varying the current; a permanent magnet's cannot.
Reversible poles
Its poles can be reversed by reversing the current.
Very strong
It can be made far stronger than an ordinary permanent magnet.
Notes: The four advantages of an electromagnet: switchable, adjustable, reversible, and can be very strong.

## Slide 11
QUIZ 1
Check Your Understanding
4 questions • think before the answer reveals on the next slide

## Slide 12
QUIZ QUESTION
Q1 — Oersted
A compass placed under a straight wire deflects only when:
A
The wire is made of iron
B
A current flows through the wire
C
The wire is very long
D
The compass is heated

## Slide 13
ANSWER REVEALED
Q1 — Oersted
A compass placed under a straight wire deflects only when:
A
The wire is made of iron
✓
A current flows through the wire
C
The wire is very long
D
The compass is heated
WHY
Oersted showed that a current produces a magnetic field. With no current there is no field, so the needle stays pointing north; switch the current on and it deflects.

## Slide 14
QUIZ QUESTION
Q2 — Reverse It
If the current in a solenoid is reversed, its magnetic poles:
A
Disappear
B
Stay the same
C
Swap over (N becomes S)
D
Become stronger

## Slide 15
ANSWER REVEALED
Q2 — Reverse It
If the current in a solenoid is reversed, its magnetic poles:
A
Disappear
B
Stay the same
✓
Swap over (N becomes S)
D
Become stronger
WHY
The direction of the field follows the current. Reversing the current reverses the field, so the north and south ends of the solenoid interchange.

## Slide 16
QUIZ QUESTION
Q3 — Stronger Magnet
Which change would NOT make an electromagnet stronger?
A
Increasing the current
B
Adding more turns of wire
C
Using a soft-iron core
D
Using a wooden core instead of iron

## Slide 17
ANSWER REVEALED
Q3 — Stronger Magnet
Which change would NOT make an electromagnet stronger?
A
Increasing the current
B
Adding more turns of wire
C
Using a soft-iron core
✓
Using a wooden core instead of iron
WHY
Wood is non-magnetic, so it adds nothing — far weaker than soft iron. Strength is increased by more current, more turns and a soft-iron core.

## Slide 18
QUIZ QUESTION
Q4 — Why Soft Iron?
An electromagnet uses a soft-iron core rather than steel because soft iron:
A
Stays magnetised permanently
B
Loses its magnetism as soon as the current stops, so the magnet can be switched off
C
Is a good conductor
D
Is lighter

## Slide 19
ANSWER REVEALED
Q4 — Why Soft Iron?
An electromagnet uses a soft-iron core rather than steel because soft iron:
A
Stays magnetised permanently
✓
Loses its magnetism as soon as the current stops, so the magnet can be switched off
C
Is a good conductor
D
Is lighter
WHY
Soft iron magnetises and demagnetises easily, so the electromagnet works only while current flows. Steel would keep its magnetism and could not be switched off.

## Slide 20
2
PART 2
Using Electromagnets
From scrapyards to doorbells

## Slide 21
USES
Uses of Electromagnets
Lifting magnets
Cranes in scrapyards lift and drop heavy iron by switching the magnet on and off.
Electric bell
An electromagnet repeatedly pulls a clapper to strike the gong.
Relays
A small current's electromagnet switches on a much larger circuit.
Loudspeakers
A changing current in a coil moves a cone to make sound.
Notes: Each use exploits the switchable, controllable magnetism. The lifting magnet and electric bell are the classic examples.

## Slide 22
ELECTRIC BELL
How an Electric Bell Works
A make-and-break circuit
• Pressing the switch completes the circuit and the electromagnet is energised.
• It attracts the soft-iron armature, so the hammer strikes the gong.
• This movement breaks the circuit at a contact, switching the magnet off.
• A spring pulls the armature back, the contact remakes, and the cycle repeats rapidly.
Notes: The make-and-break action is the heart of the bell: the magnet switches itself off as the hammer moves, then on again.

## Slide 23
WRAP UP
Quick Recap
✓ Oersted — a current produces a magnetic field
✓ Straight wire — circular field lines; right-hand thumb rule
✓ Loop & solenoid — concentrate the field; solenoid acts like a bar magnet
✓ Electromagnet — solenoid + soft-iron core; switchable and strong
✓ Advantages — switchable, adjustable, reversible, very strong
✓ Uses — lifting magnets, electric bell, relays, loudspeakers
Notes: Rapid recap; the right-hand rule and the electromagnet advantages are the key recall items.

## Slide 24
QUIZ 2
Final Check — Fields & Electromagnets
5 questions • think before the answer reveals on the next slide

## Slide 25
QUIZ QUESTION
Q1 — Field Shape
The magnetic field lines around a long straight current-carrying wire are:
A
Straight lines along the wire
B
Concentric circles around the wire
C
Radial lines pointing outward
D
There is no field

## Slide 26
ANSWER REVEALED
Q1 — Field Shape
The magnetic field lines around a long straight current-carrying wire are:
A
Straight lines along the wire
✓
Concentric circles around the wire
C
Radial lines pointing outward
D
There is no field
WHY
The field circles the wire. Closer to the wire the circles are tighter (stronger field); the right-hand thumb rule gives their direction.

## Slide 27
QUIZ QUESTION
Q2 — Scrapyard Crane
A scrapyard uses an electromagnet rather than a permanent magnet to move cars mainly because it can:
A
Never lose strength
B
Be switched off to drop the load
C
Work without electricity
D
Lift wood and plastic too

## Slide 28
ANSWER REVEALED
Q2 — Scrapyard Crane
A scrapyard uses an electromagnet rather than a permanent magnet to move cars mainly because it can:
A
Never lose strength
✓
Be switched off to drop the load
C
Work without electricity
D
Lift wood and plastic too
WHY
The whole point is control: turn the current on to grab the scrap and off to release it. A permanent magnet could never let go.

## Slide 29
QUIZ QUESTION
Q3 — Doorbell Buzz
An electric bell rings continuously while the button is pressed because the circuit:
A
Stays permanently closed
B
Repeatedly makes and breaks itself as the hammer moves
C
Has no electromagnet
D
Uses a permanent magnet

## Slide 30
ANSWER REVEALED
Q3 — Doorbell Buzz
An electric bell rings continuously while the button is pressed because the circuit:
A
Stays permanently closed
✓
Repeatedly makes and breaks itself as the hammer moves
C
Has no electromagnet
D
Uses a permanent magnet
WHY
As the armature is attracted, it breaks the contact and the magnet switches off; a spring returns it, remaking the contact. This rapid make-and-break keeps the hammer striking.

## Slide 31
QUIZ QUESTION
Q4 — More Turns
Doubling the number of turns on a solenoid (same current) makes its magnetic field:
A
Weaker
B
Stronger
C
Reverse direction
D
Disappear

## Slide 32
ANSWER REVEALED
Q4 — More Turns
Doubling the number of turns on a solenoid (same current) makes its magnetic field:
A
Weaker
✓
Stronger
C
Reverse direction
D
Disappear
WHY
More turns means more current loops adding their fields together, so the solenoid's magnetic field becomes stronger.

## Slide 33
QUIZ QUESTION
Q5 — Compass Test
A solenoid hangs freely and comes to rest pointing north–south. This proves the solenoid:
A
Is made of iron
B
Behaves like a bar magnet with N and S poles
C
Carries no current
D
Is an insulator

## Slide 34
ANSWER REVEALED
Q5 — Compass Test
A solenoid hangs freely and comes to rest pointing north–south. This proves the solenoid:
A
Is made of iron
✓
Behaves like a bar magnet with N and S poles
C
Carries no current
D
Is an insulator
WHY
Only a magnet aligns itself north–south in the Earth's field. Since the current-carrying solenoid does so, it must have north and south poles like a bar magnet.

## Slide 35
Electricity That Magnetises
A simple coil and a current give us magnets we can switch, tune and reverse at will.