## Slide 1
ICSE • CLASS 10 • MAGNETISM
Motors & Induction
Force on a conductor • The DC motor • Electromagnetic induction • Generators

## Slide 2
INTRODUCTION
Learning Objectives
1
State the force on a current-carrying conductor in a field
2
Apply Fleming's left-hand rule
3
Explain how a simple DC motor works
4
Describe electromagnetic induction
5
State Faraday's laws of electromagnetic induction
6
Outline how a generator and a transformer work
Notes: Open by previewing these objectives so students know what they should be able to do by the end of the session.

## Slide 3
1
PART 1
The Motor Effect
When a current feels a force in a magnetic field

## Slide 4
MOTOR EFFECT
Force on a Conductor
Opposite forces on the two sides of the coil
Current + field → force
• A current-carrying conductor placed in a magnetic field experiences a force.
• The force is largest when the conductor is at right angles to the field.
• It is bigger for a stronger field, a larger current or a longer conductor.
• Reversing the current — or the field — reverses the direction of the force.
Notes: The motor effect. Force depends on field, current and length, and is maximum at 90°. This drives the motor.

## Slide 5
FLEMING
Fleming's Left-Hand Rule
Fleming's left-hand rule gives the direction of the force on the conductor.
• Hold the thumb, first finger and second finger of the left hand at right angles.
• First finger → Field, seCond finger → Current, thuMb → Motion (force).
• Use it for motors — anything that is made to move.
Notes: Teach the mnemonic: First=Field, seCond=Current, thuMb=Motion. Left hand for motors.

## Slide 6
DC MOTOR
The Simple DC Motor
The commutator keeps the rotation going one way
Turning electricity into motion
• A rectangular coil sits between the poles of a magnet.
• Current flows in opposite directions along the two sides, so they feel opposite forces.
• This pair of forces makes the coil rotate.
• A split-ring commutator reverses the current every half turn, keeping it spinning the same way.
Notes: The commutator is the crucial part — it flips the current each half turn so the coil keeps turning continuously.

## Slide 7
QUIZ 1
Check Your Understanding
5 questions • think before the answer reveals on the next slide

## Slide 8
QUIZ QUESTION
Q1 — Which Hand?
To find the direction in which a motor's coil is pushed, you use:
A
Fleming's right-hand rule
B
Fleming's left-hand rule
C
The right-hand thumb rule
D
Ohm's law

## Slide 9
ANSWER REVEALED
Q1 — Which Hand?
To find the direction in which a motor's coil is pushed, you use:
A
Fleming's right-hand rule
✓
Fleming's left-hand rule
C
The right-hand thumb rule
D
Ohm's law
WHY
The left-hand rule gives the direction of force (motion) on a current in a field — used for motors. The right-hand rule is for induced currents in generators.

## Slide 10
QUIZ QUESTION
Q2 — No Force
A current-carrying wire lies exactly parallel to the magnetic field. The force on it is:
A
Maximum
B
Zero
C
Half the maximum
D
Reversed

## Slide 11
ANSWER REVEALED
Q2 — No Force
A current-carrying wire lies exactly parallel to the magnetic field. The force on it is:
A
Maximum
✓
Zero
C
Half the maximum
D
Reversed
WHY
The motor effect is greatest when the wire is at 90° to the field and zero when it lies along the field. Parallel to the field, there is no force.

## Slide 12
QUIZ QUESTION
Q3 — Reverse Both
In a motor, both the current AND the magnetic field are reversed at the same time. The coil now turns:
A
The opposite way
B
The same way as before
C
Twice as fast
D
It stops

## Slide 13
ANSWER REVEALED
Q3 — Reverse Both
In a motor, both the current AND the magnetic field are reversed at the same time. The coil now turns:
A
The opposite way
✓
The same way as before
C
Twice as fast
D
It stops
WHY
Reversing the current alone, or the field alone, flips the force. Reversing both flips it twice — back to the original direction — so the coil turns the same way.

## Slide 14
QUIZ QUESTION
Q4 — Commutator's Job
The split-ring commutator in a DC motor is needed to:
A
Increase the voltage
B
Reverse the current in the coil every half turn so it keeps rotating one way
C
Stop the coil
D
Cool the motor

## Slide 15
ANSWER REVEALED
Q4 — Commutator's Job
The split-ring commutator in a DC motor is needed to:
A
Increase the voltage
✓
Reverse the current in the coil every half turn so it keeps rotating one way
C
Stop the coil
D
Cool the motor
WHY
Without it, the coil would stop after a half turn. The commutator flips the current direction at just the right moment so the forces keep driving the coil the same way round.

## Slide 16
QUIZ QUESTION
Q5 — Speed It Up
Which change would make a simple DC motor spin faster?
A
Using a weaker magnet
B
Increasing the current through the coil
C
Using fewer turns on the coil
D
Removing the commutator

## Slide 17
ANSWER REVEALED
Q5 — Speed It Up
Which change would make a simple DC motor spin faster?
A
Using a weaker magnet
✓
Increasing the current through the coil
C
Using fewer turns on the coil
D
Removing the commutator
WHY
A larger current means a bigger force on each side of the coil, turning it more strongly and faster. A stronger magnet or more turns would help too; a weaker magnet or fewer turns would slow it.

## Slide 18
2
PART 2
Electromagnetic Induction
Magnetism making electricity

## Slide 19
INDUCTION
Electromagnetic Induction
Move the magnet → the galvanometer deflects
A changing field makes a current
• Moving a magnet into or out of a coil makes a current flow in the coil.
• No battery is needed — the changing magnetic field 'induces' the current.
• A galvanometer deflects, showing the induced current.
• Stop moving the magnet and the current stops — only a change induces it.
Notes: Induction is the reverse of the motor effect. Key word: CHANGE. A stationary magnet induces nothing.

## Slide 20
FARADAY
Faraday's Laws of Induction
Faraday summarised electromagnetic induction in two laws.
• First law: an EMF is induced whenever the magnetic field through a coil changes.
• Second law: the size of the induced EMF is greater when the field changes faster.
• More turns, a stronger magnet and faster movement all increase the induced EMF.
Notes: Faraday: a change of field induces an EMF; faster change (or more turns) gives a bigger EMF.

## Slide 21
BIGGER EMF
How to Increase the Induced Current
Move faster
A quicker change of the magnetic field induces a larger EMF.
More turns
A coil with more turns gives a bigger induced EMF.
Stronger magnet
A more powerful magnet increases the change in field.
No movement, no EMF
If nothing changes, no current is induced.
Notes: The factors that increase induced EMF — all are about a bigger or faster change of field.

## Slide 22
FLEMING (RIGHT)
Fleming's Right-Hand Rule
For induction (generators) we use the RIGHT hand to find the direction of the induced current.
• Hold thumb, first finger and second finger of the RIGHT hand at right angles.
• First finger → Field, thuMb → Motion, seCond finger → induced Current.
• Left hand for motors (force); right hand for generators (induced current).
Notes: Pair this with the left-hand rule: left = motor (force), right = generator (induced current). A frequent point of confusion.

## Slide 23
GENERATOR & TRANSFORMER
Two Machines From Induction
AC generator
A coil spun in a magnetic field induces an alternating current — how power stations make electricity.
Slip rings
Connect the spinning coil to the outside circuit, giving AC.
Transformer
Uses a changing current in one coil to induce a voltage in another.
Step up / down
More turns on the output coil step the voltage up; fewer step it down.
Notes: Generator: motion → electricity (induction). Transformer: changes AC voltage using two coils and a changing field.

## Slide 24
WRAP UP
Quick Recap
✓ Motor effect — current in a field feels a force
✓ Fleming's left hand — Field, Current, Motion — for motors
✓ DC motor — opposite forces turn a coil; commutator keeps it going
✓ Induction — a changing field induces a current — no battery
✓ Faraday — EMF appears on change; faster change → bigger EMF
✓ Generator & transformer — make AC, and step voltage up or down
Notes: Rapid recap; contrast the motor effect (left hand) with induction (right hand / generators).

## Slide 25
QUIZ 2
Final Check — Induction & Machines
5 questions • think before the answer reveals on the next slide

## Slide 26
QUIZ QUESTION
Q1 — Make It Deflect
A bar magnet is held still inside a coil connected to a galvanometer. The galvanometer reads zero because:
A
The magnet is too weak
B
There is no change in the magnetic field, so no EMF is induced
C
The coil has too few turns
D
The wire is broken

## Slide 27
ANSWER REVEALED
Q1 — Make It Deflect
A bar magnet is held still inside a coil connected to a galvanometer. The galvanometer reads zero because:
A
The magnet is too weak
✓
There is no change in the magnetic field, so no EMF is induced
C
The coil has too few turns
D
The wire is broken
WHY
Induction needs a CHANGING field. A motionless magnet gives a steady field through the coil, so nothing is induced. Move it and the needle springs to life.

## Slide 28
QUIZ QUESTION
Q2 — Bigger Kick
Which would give the largest deflection on the galvanometer?
A
Pushing a weak magnet in slowly
B
Pushing a strong magnet in quickly
C
Holding a strong magnet still
D
Removing the coil

## Slide 29
ANSWER REVEALED
Q2 — Bigger Kick
Which would give the largest deflection on the galvanometer?
A
Pushing a weak magnet in slowly
✓
Pushing a strong magnet in quickly
C
Holding a strong magnet still
D
Removing the coil
WHY
The induced EMF grows with a stronger magnet and a faster change. A strong magnet moved quickly maximises both, giving the biggest deflection.

## Slide 30
QUIZ QUESTION
Q3 — Motor or Generator?
A device that converts electrical energy into motion is a motor. A device that converts motion into electrical energy is a:
A
Transformer
B
Generator
C
Resistor
D
Fuse

## Slide 31
ANSWER REVEALED
Q3 — Motor or Generator?
A device that converts electrical energy into motion is a motor. A device that converts motion into electrical energy is a:
A
Transformer
✓
Generator
C
Resistor
D
Fuse
WHY
A generator does the reverse of a motor: spinning a coil in a field induces a current, turning mechanical motion into electrical energy.

## Slide 32
QUIZ QUESTION
Q4 — Transformer Needs AC
A transformer works only with alternating current because it relies on:
A
A steady current
B
A continually changing magnetic field to induce a voltage in the second coil
C
A permanent magnet
D
A commutator

## Slide 33
ANSWER REVEALED
Q4 — Transformer Needs AC
A transformer works only with alternating current because it relies on:
A
A steady current
✓
A continually changing magnetic field to induce a voltage in the second coil
C
A permanent magnet
D
A commutator
WHY
Induction needs change. AC constantly changes, so it keeps the field through the second coil changing and a voltage is induced. A steady DC current would induce nothing.

## Slide 34
QUIZ QUESTION
Q5 — Step Up
A transformer has more turns on its output (secondary) coil than on its input. It will:
A
Step the voltage down
B
Step the voltage up
C
Leave the voltage unchanged
D
Stop the current

## Slide 35
ANSWER REVEALED
Q5 — Step Up
A transformer has more turns on its output (secondary) coil than on its input. It will:
A
Step the voltage down
✓
Step the voltage up
C
Leave the voltage unchanged
D
Stop the current
WHY
The voltage shares out in proportion to the turns. More turns on the secondary than the primary means a higher output voltage — a step-up transformer.

## Slide 36
Motion and Electricity, Two Ways
A current in a field moves a motor; a moving magnet powers a city — electromagnetism runs the modern world.